CONTENTS

Report Volume - I

Foreword

Check list

Salient Features

Executive Summary

List of officers associated in preparation of DPR

Index Map

| Para no. | Particulars | Page no. |
| --- | --- | --- |
|  | Chapter – I : Introduction |  |
| 1.0 | General | 1 |
| 1.1 | Outline of the project | 1 |
| 1.2 | Justification and objective of the project | 2 |
| 1.3 | Lesson learned from Previous Projects | 3 |
| 1.4 | National Perspective Plan for Water Resources Development | 5 |
| 1.5 | MoU between Centre and States & Inter State Aspects | 6 |
| 1.6 | Selection of Proposed schemes | 8 |
| 1.7 | Project Planning and Optimization of Benefits | 12 |
| 1.8 | Approach Adopted | 14 |
| 1.8.1 | Surveys & Investigations works done departmentally | 14 |
| 1.8.2 | Surveys & Investigations carried out by other agencies | 15 |
| 1.8.2.1 | Borrow area survey, geotechnical investigation, construction Material survey, testing of rock samples | 15 |
| 1.8.2.2 | Geological Survey | 15 |
| 1.8.2.3 | Drilling Works | 15 |
| 1.8.2.4 | Submergence area survey of Neemkheda / Makodia Dam | 15 |
| 1.8.2.5 | Feasibility studies of upper Betwa Projects by Remote Sensing Techniques | 15 |
| 1.8.2.6 | Reservoir Survey of Daudhan Dam and Command area survey of Ken command in M.P. | 16 |
| 1.8.3 | Technical Studies | 16 |
| 1.8.3.1 | Design of important project components and writing of Design chapters | 16 |
| 1.8.3.2 | Irrigation Planning studies | 16 |
| 1.8.3.3 | Construction Planning, Equipment Planning and Manpower Planning | 17 |
| 1.8.3.4 | Hydrological Studies | 17 |
| 1.8.3.5 | Power Potential and E&M Studies | 17 |
| 1.8.3.6 | Study of Seismic Parameters | 17 |
| 1.8.3.7 | Petrographic Analysis of Slit samples | 17 |
| Para no. | Particulars | Page no. |
| 1.8.4 | Socio-economic Survey, Environmental Impact Assessment Study | 17 |
| 1.8.5 | Monitoring Mechanism | 18 |
| 1.9 | Methodology Adopted | 18 |
| 1.9.1 | Data collection | 18 |
| 1.9.2 | Planning and Layout | 19 |
| 1.9.2.1 | Daudhan Dam Complex | 19 |
| 1.9.2.2 | Makodia dam complex | 19 |
| 1.9.2.3 | Barari Barrage | 20 |
| 1.9.2.4 | Kesari Barrage | 20 |
| 1.9.3 | Surveys & Investigations | 20 |
| 1.9.4 | Engineering assessments and Front end engineering | 21 |
| 1.9.5 | Ecological, Socio-economic and Financial Aspects | 22 |
| 1.10 | Financial and Economic Analysis | 26 |
| 1.11 | Clearances Required | 26 |
| Fig.1.1 | Layout plan of Daudhan reservoir | 28 |
|  | Chapter – II : Surveys & Investigations |  |
| 2.0 | Main Components | 29 |
| 2.0.1 | Background for changes in DPR | 31 |
| 2.0.1.1 | Daudhan dam and Spillway | 31 |
| 2.0.1.2 | Tunnels and Power House I & II | 31 |
| 2.0.1.3 | Link Canal | 32 |
| 2.0.1.4 | Upper Betwa Projects | 32 |
| 2.1 | Topographical Surveys | 33 |
| 2.1.1 | Topographical surveys for Daudhan dam & Link Canal | 33 |
| 2.1.1.1 | River | 33 |
| 2.1.1.2 | Reservoir | 34 |
| 2.1.1.3 | Headworks | 34 |
| 2.1.1.4 | Plant and Colony Layout | 35 |
| 2.1.1.5 | Canal and Water Conductor System and Canal Structures | 35 |
| 2.1.1.6 | Powerhouse, Switchyards, Surge-shaft, Tailrace, etc. | 36 |
| 2.1.1.7 | Tunnels, Adits and Penstocks | 38 |
| 2.1.1.8 | Command Area Survey | 39 |
| 2.1.1.9 | Soil Conservation | 40 |
| 2.1.1.10 | Any other | 40 |
| 2.1.2 | Other Allied Surveys | 40 |
| 2.1.2.1 | Archaeological Surveys in the Reservoir Area | 40 |
| 2.1.2.2 | Mineral (useful and harmful) Surveys in the Catchment/ Reservoir Areas | 40 |
| 2.1.2.3 | Right of Way surveys for the Reservoir | 40 |
| 2.1.2.4 | Communication Surveys | 41 |
| Para no. | Particulars | Page no. |
| 2.1.2.5 | Drainage surveys | 41 |
| 2.1.2.6 | Soil surveys | 42 |
| 2.1.3 | Geology, Geophysical & Seismic Investigations | 42 |
| 2.1.3.1 | Geology | 42 |
| 2.1.3.2 | Seismicity | 44 |
| 2.1.4 | Foundation Investigations | 45 |
| 2.1.4.1 | Earth Dam | 45 |
| 2.1.4.2 | Concrete dam in Spill Way Portion | 46 |
| 2.1.4.3 | Canal and Canal Structures | 46 |
| 2.1.4.4 | Power House and Tunnels | 47 |
| 2.1.5 | Geo technical Investigations and Borrow area (soil) Surveys and Construction Material Investigations | 48 |
| 2.1.5.1 | Borrow Area Survey - Soils | 48 |
| 2.1.5.2 | Sand | 49 |
| 2.1.5.3 | Rock and Aggregates | 50 |
| 2.1.5.4 | Bricks, Tiles | 51 |
| 2.1.5.5 | Pozzolona | 51 |
| 2.1.5.6 | Cement / Lime Stone | 51 |
| 2.1.5.7 | Cement and Steel | 51 |
| 2.1.5.8 | Scarce Material | 51 |
| 2.1.5.9 | Any other Material | 51 |
| 2.1.6 | Hydrological and Meteorological Investigations | 51 |
| 2.1.6.1 | Rainfall | 51 |
| 2.1.6.2 | Sunshine, Cloud Cover and Visibility | 52 |
| 2.1.6.3 | Wind and Cyclones | 52 |
| 2.1.6.4 | Humidity | 52 |
| 2.1.6.5 | Temperature | 52 |
| 2.1.6.6 | Discharge | 52 |
| 2.1.6.7 | Sedimentation | 53 |
| 2.1.6.8 | Water Quality | 53 |
| 2.1.6.9 | Evaporation | 53 |
| 2.2.1 | Topographical Surveys of Makodia / Neemkheda dam | 55 |
| 2.2.1.1 | River | 55 |
| 2.2.1.2 | Reservoir | 55 |
| 2.2.1.3 | Headworks | 56 |
| 2.2.1.4 | Plant and Colony Layout | 56 |
| 2.2.1.5 | Canal and Water Conductor System and Canal Structures | 56 |
| 2.2.1.6 | Powerhouse, Switchyards, Surge-shaft, Tailrace, etc. | 58 |
| 2.2.1.7 | Tunnel, Adits and Penstocks | 59 |
| 2.2.1.8 | Command Area Survey | 58 |
| 2.2.1.9 | Soils Conservation | 58 |
| 2.2.1.10 | Any other | 59 |
| Para no. | Particulars | Page no. |
| 2.2.2 | Other Allied Surveys | 60 |
| 2.2.2.1 | Archaeological Surveys in the Reservoir Area | 60 |
| 2.2.2.2 | Mineral (useful and harmful) Surveys in the Catchment/Reservoir Areas | 60 |
| 2.2.2.3 | Right of Way Surveys for the Reservoir | 60 |
| 2.2.2.4 | Communication Survey | 60 |
| 2.2.2.5 | Drainage Surveys | 61 |
| 2.2.2.6 | Soil Surveys | 61 |
| 2.2.3 | Geology, Geophysical & Seismic Investigation | 61 |
| 2.2.3.1 | Geology | 61 |
| 2.2.3.2 | Seismicity | 62 |
| 2.2.4 | Foundation Investigations | 63 |
| 2.2.4.1 | Earth dam | 63 |
| 2.2.4.2 | Concrete dam in Spillway Portion | 63 |
| 2.2.4.3 | Canal and Canal Structures | 64 |
| 2.2.4.4 | Power House and Tunnels | 64 |
| 2.2.5 | Geo-technical Investigations and Borrow area (soil) Surveys and Construction Material Investigations | 64 |
| 2.2.5.1 | Borrow Area Survey - Soils | 64 |
| 2.2.5.2 | Sand | 65 |
| 2.2.5.3 | Rock and Aggregate | 65 |
| 2.2.5.4 | Bricks, Tiles | 66 |
| 2.2.5.5 | Pozzolona | 66 |
| 2.2.5.6 | Cement / Lime Stone | 66 |
| 2.2.5.7 | Cement and Steel | 66 |
| 2.2.5.8 | Scarce Materials | 66 |
| 2.2.5.9 | Any Other Material | 67 |
| 2.2.6 | Hydrological and Meteorological Investigations | 67 |
| 2.2.6.1 | Rainfall and Runoff | 67 |
| 2.2.6.2 | Sunshine, Cloud Cover and Visibility | 67 |
| 2.2.6.3 | Wind and Cyclones | 67 |
| 2.2.6.4 | Humidity | 67 |
| 2.2.6.5 | Temperature | 67 |
| 2.2.6.6 | Discharge | 67 |
| 2.2.6.7 | Sedimentation | 68 |
| 2.2.6.8 | Water Quality | 68 |
| 2.2.6.9 | Evaporation | 68 |
| 2.3.1 | Topographical Surveys of Barari Barrage | 69 |
| 2.3.1.1 | River | 69 |
| 2.3.1.2 | Reservoir / Pond | 69 |
| 2.3.1.3 | Headworks | 70 |
| 2.3.1.4 | Plant and Colony layout | 70 |
| Para no. | Particulars | Page no. |
| 2.3.1.5 | Canal and Water Conductor System and Canal Structures | 70 |
| 2.3.1.6 | Powerhouse, Switchyards, Surge-Shaft, Tailrace, etc. | 70 |
| 2.3.1.7 | Tunnel, Adits and Penstocks | 71 |
| 2.3.1.8 | Command Area Survey | 71 |
| 2.3.1.9 | Soil conservation | 71 |
| 2.3.1.10 | Any other | 71 |
| 2.3.2 | Other Allied Surveys | 72 |
| 2.3.2.1 | Archaeological surveys in the reservoir area | 72 |
| 2.3.2.2 | Mineral (useful and harmful) Surveys in the Catchment /Reservoir Area | 72 |
| 2.3.2.3 | Right of Way Survey for the Reservoir | 72 |
| 2.3.2.4 | Communication Surveys | 72 |
| 2.3.2.5 | Drainage Surveys | 72 |
| 2.3.2.6 | Soil Surveys | 73 |
| 2.3.3 | Geology, Geophysical & Seismic Investigations | 73 |
| 2.3.3.1 | Geology | 73 |
| 2.3.3.2 | Seismicity | 74 |
| 2.3.4 | Foundation Investigations | 74 |
| 2.3.4.1 | Earth and Rock Fill Dam | 74 |
| 2.3.4.2 | Barrage | 74 |
| 2.3.4.3 | Canal and Canal Structures | 74 |
| 2.3.4.4 | Power House and Tunnels | 75 |
| 2.3.5 | Geo-technical Investigations and Borrow Area (soil) Surveys and Construction Material Investigations | 75 |
| 2.3.5.1 | Soils | 75 |
| 2.3.5.2 | Sand | 75 |
| 2.3.5.3 | Rock and Aggregates | 75 |
| 2.3.5.4 | Bricks, Tiles | 76 |
| 2.3.5.5 | Pozzolona | 76 |
| 2.3.5.6 | Cement / Lime Stone | 76 |
| 2.3.5.7 | Cement and Steel | 76 |
| 2.3.5.8 | Scarce Materials | 77 |
| 2.3.5.9 | Any Other Material | 77 |
| 2.3.6 | Hydrological and Meteorological Investigations | 77 |
| 2.3.6.1 | Rainfall and Runoff | 77 |
| 2.3.6.2 | Sunshine, Cloud Cover and Visibility | 77 |
| 2.3.6.3 | Wind and Cyclones | 77 |
| 2.3.6.4 | Humidity | 77 |
| 2.3.6.5 | Temperature | 77 |
| 2.3.6.6 | Discharge | 78 |
| 2.3.6.7 | Sedimentation | 78 |
| 2.3.6.8 | Water quality | 78 |
| Para no. | Particulars | Page no. |
| 2.3.6.9 | Evaporation | 78 |
| 2.4.1 | Topographical Surveys of Kesari Barrage | 79 |
| 2.4.1.1 | River | 79 |
| 2.4.1.2 | Reservoir | 79 |
| 2.4.1.3 | Headworks | 80 |
| 2.4.1.4 | Plant and Colony Layout | 80 |
| 2.4.1.5 | Canal and Water Conductor System and Canal Structures | 80 |
| 2.4.1.6 | Powerhouse, Switchyards, Surge-shaft, Tailrace, etc. | 81 |
| 2.4.1.7 | Tunnel, Adits and Penstocks | 81 |
| 2.4.1.8 | Command Area Survey | 81 |
| 2.4.1.9 | Soil Conservation | 81 |
| 2.4.1.10 | Any other | 82 |
| 2.4.2 | Other Allied Surveys | 82 |
| 2.4.2.1 | Archaeological surveys in the reservoir area | 82 |
| 2.4.2.2 | Mineral (useful and harmful) Surveys in the Catchment and Reservoir Areas | 82 |
| 2.4.2.3 | Right of Way Surveys for the Reservoir | 82 |
| 2.4.2.4 | Communication Surveys | 82 |
| 2.4.2.5 | Drainage Surveys | 83 |
| 2.4.2.6 | Soil Surveys | 83 |
| 2.4.3 | Geology, Geophysical & Seismic Investigations | 83 |
| 2.4.3.1 | Geology | 83 |
| 2.4.3.2 | Seismicity | 84 |
| 2.4.3 | Foundation Investigations | 84 |
| 2.4.4.1 | Earth and Rock fill Dam | 84 |
| 2.4.4.2 | Barrage | 84 |
| 2.4.4.3 | Canal | 85 |
| 2.4.4.4 | Powerhouse, Tunnels and Canal Structures | 85 |
| 2.4.5 | Geo-technical Investigations and Borrow Area (soil) Surveys and Construction Material Investigations | 85 |
| 2.4.5.1 | Soils | 85 |
| 2.4.5.2 | Sand | 85 |
| 2.4.5.3 | Rock and Aggregates | 86 |
| 2.4.5.4 | Bricks, Tiles | 86 |
| 2.4.5.5 | Pozzolona | 86 |
| 2.4.5.6 | Cement / Lime Stone | 87 |
| 2.4.5.7 | Cement and Steel | 87 |
| 2.4.5.8 | Scarce materials | 87 |
| 2.4.5.9 | Any Other Material | 87 |
| 2.4.6 | Hydrological and Meteorological Investigations | 87 |
| 2.4.6.1 | Rainfall and Runoff | 87 |
| 2.4.6.2 | Sunshine, Cloud Cover and Visibility | 87 |
| Para no. | Particulars | Page no. |
| 2.4.6.3 | Wind and Cyclones | 87 |
| 2.4.6.4 | Humidity | 88 |
| 2.4.6.5 | Temperature | 88 |
| 2.4.6.6 | Discharge | 88 |
| 2.4.6.7 | Sedimentation | 88 |
| 2.4.6.8 | Water quality | 88 |
| 2.4.6.9 | Evaporation | 88 |
|  | Chapter – III : Hydrology and Water Assessment |  |
| 3.0 | General Climate and Hydrology | 89 |
| 3.1 | General information about regions | 89 |
| 3.1.1 | Specific information | 90 |
| 3.1.1.1 | Drainage Basin | 90 |
| 3.1.1.2 | Command Area | 91 |
| 3.1.1.3 | Floods and drainage | 94 |
| 3.1.1.4 | River Geometry | 94 |
| 3.1.1.5 | Ground Water Recharge | 97 |
| 3.1.1.6 | Reservoir Area | 97 |
| 3.1.1.7 | Other Water Usage | 98 |
| 3.1.1.8 | Navigation | 98 |
| 3.1.2 | Data Availability | 98 |
| 3.1.2.1 | Rainfall and Snowfall | 98 |
| 3.1.2.2 | Pan Evaporation | 101 |
| 3.1.2.3 | Climatological parameters like temperature, humidity, wind etc. | 101 |
| 3.1.2.4 | River Gauge and discharge | 102 |
| 3.1.2.5 | Sediment (suspended and bed load) inflow and grain size composition | 102 |
| 3.1.2.6 | Water quality | 102 |
| 3.2 | Hydrological Data Requirement | 102 |
| 3.2.1 | Alternatives and classifications | 102 |
| 3.2.2 | Inputs | 103 |
| 3.2.2.1 | Type of inputs | 103 |
| 3.2.2.2 | Time units for simulation studies | 103 |
| 3.2.2.3 | Hydrological Inputs | 104 |
| 3.2.3 | Requirement of the inputs for the project | 104 |
| 3.3 | Compilation and processing of basic hydrological data | 104 |
| 3.3.1 | Hydrological investigation | 104 |
| 3.3.2 | Data from other sources | 105 |
| 3.3.3 | Processing of data | 105 |
| 3.3.3.1 | Quality of data | 105 |
| 3.3.3.2 | Filling of short data gaps | 105 |
| Para no. | Particulars | Page no. |
| 3.3.4 | Adjustment of records | 105 |
| 3.3.5 | Consistency of data | 106 |
| 3.3.5.1 | Internal | 106 |
| 3.3.5.2 | External | 108 |
| 3.3.6 | Presentation of data | 108 |
| 3.3.7 | Data for studies other than simulation | 111 |
| 3.4 | Presentation of hydrologic inputs for simulation | 111 |
| 3.4.1 | Water inflows | 111 |
| 3.4.1.1 | Storage projects | 111 |
| 3.4.2 | Extension of data | 111 |
| 3.4.3 | Data generation | 113 |
| 3.4.3.1 | Diversion and small poundage | 113 |
| 3.4.4 | Extension of data | 113 |
| 3.4.5 | Lake evaporation | 113 |
| 3.4.6 | Sedimentation studies | 113 |
| 3.4.6.1 | Revised area capacity curves | 113 |
| 3.4.6.2 | Rate of sedimentation | 116 |
| 3.4.7 | Potential evapotranspiration and rainfall | 116 |
| 3.4.8 | Flood inputs | 116 |
| 3.4.9 | Inputs for water quality | 116 |
| 3.4.10 | Low flow inputs | 117 |
| 3.4.11 | Surface to groundwater recharge | 117 |
| 3.5 | Preparation of hydrological inputs for studies other than simulation | 117 |
| 3.5.1 | Design flood for safety of structures | 117 |
| 3.5.1.1 | Criteria for selection of design flood for each structure taking into account the importance of each structure | 117 |
| 3.5.1.2 | Overall approach adopted | 118 |
| 3.5.2 | Hydro-meteorological approach | 119 |
| 3.5.3 | Frequency approach | 120 |
| 3.5.3.1 | Comparison of design flood estimates | 120 |
| 3.5.4 | Design flood for determination of flood storage & flood control works | 121 |
| 3.5.4.1 | Flood problems | 121 |
| 3.5.4.2 | Degree of protection | 122 |
| 3.5.4.3 | Design flood for fixing storage & design of structures | 122 |
| 3.5.5 | Studies for design of drainage in the command area | 122 |
| 3.5.5.1 | The problem | 122 |
| 3.5.5.2 | Surface drainage | 122 |
| 3.5.6 | Design flood for diversion arrangements | 122 |
| 3.5.7 | Studies for determination of levels for locating structures on outlets | 123 |
| Para no. | Particulars | Page no. |
| 3.5.7.1 | Location of structures | 123 |
| 3.5.7.2 | Location of outlets | 124 |
| 3.5.8 | Tail water rating curves | 126 |
| 3.6 | Simulation studies | 128 |
| 3.6.1 | Model studies | 128 |
| 3.6.2 | Project performance | 128 |
| 3.6.3 | Minimum flow for environmental considerations | 131 |
| 3.7 | Effect of project on hydrologic regime | 131 |
| 3.7.1 | Effect on low flows | 131 |
| 3.7.2 | Effect on peak floods | 131 |
| 3.7.3 | Effect on total runoff | 132 |
| 3.7.4 | Effect on sediment flows | 132 |
| 3.8 | Water allocation and interstate aspects | 133 |
| 3.8.1 | Water | 133 |
| 3.8.2 | Power | 133 |
| 3.8.3 | Other aspects | 134 |
|  | Chapter – IV : Design aspects |  |
| 4.1 | Engineering Assessment | 135 |
| 4.1.1 | General | 135 |
| 4.1.2 | Geology, Seismicity & foundation | 136 |
| 4.1.3 | Alternative studies carried out for selection of sites & type of structures | 139 |
| 4.1.4 | Choice of final layout of all major components of the project and reason | 141 |
| 4.1.5 | Design flood and sediment studies | 142 |
| 4.1.6 | Free board | 143 |
| 4.1.7 | River diversion arrangement | 143 |
| 4.1.8 | Construction material-brief | 145 |
| 4.1.9 | Details of the model studies for important structures | 146 |
| 4.2 | Daudhan dam | 147 |
| 4.2.1 | Daudhan earth dam | 147 |
| 4.2.2 | Daudhan concrete dam/non over flow section /stability analysis/spillway section | 150 |
| 4.2.3 | Openings through Daudhan Dam | 154 |
| 4.3 | Canals from Daudhan Dam | 155 |
| 4.3.1 | Description of canal systems including ridge/contour/lift canal capacity and considerations for fixing alignments etc. | 155 |
| 4.3.2 | Study of integrated network of canal system and its operation to utilize the water potential of streams crossed by main canal system by provision of storage/tail tank etc. | 161 |
| Para no. | Particulars | Page no. |
| 4.3.2.1 | Description of soil profile along the canal alignment based on pit/auger holes | 161 |
| 4.3.2.2 | Evaluation of the Design parameters based on the samples collected along the canal alignment, borrow area and suggested treatment for problematic reaches. | 162 |
| 4.3.2.3 | Details of lining | 163 |
| 4.3.2.4 | Transmission losses assumed for lined/unlined channel | 163 |
| 4.3.2.5 | Cut off statement showing the details of the discharge required from tail to the head considering the irrigation requirement and transmission losses in taking of channel of distributaries out falling from KB link canal | 163 |
| 4.3.2.6 | Design calculation for adequacy of canal selections adopted | 163 |
| 4.3.2.7 | Design discharge data (irrigation requirement, transmission losses, evaporation losses etc.) for each distributaries supported by detailed calculation for a representative distributary. | 164 |
| 4.3.2.8 | Canal structures across Ken-Betwa link canal | 165 |
| 4.3.2.9 | Description of canal systems including ridge/contour/lift canal capacity and considerations for fixing alignments etc. | 169 |
| 4.4 | Power House | 171 |
| 4.4.1 | Alternative studies | 171 |
| 4.4.1.1 | Power House – I | 172 |
| 4.4.1.2 | Power House – II | 172 |
| 4.4.1.3 | Upper Level Tunnel | 172 |
| 4.4.2 | Dam-Toe Power House (PH-1) | 172 |
| 4.4.2.1 | Intake | 173 |
| 4.4.2.2 | Power channel | 175 |
| 4.4.2.3 | Tunnels/Pressure shafts | 175 |
| 4.4.2.4 | Balancing Reservoir | 175 |
| 4.4.2.5 | Fore Bay | 175 |
| 4.4.2.6 | Penstocks and surge shaft | 175 |
| 4.4.2.7 | Surface power house (PH-I) | 176 |
| 4.4.3 | Lower Level Tunnel Power House-II | 178 |
| 4.4.3.1 | Intake for Power house - II | 178 |
| 4.4.3.2 | Power channel | 179 |
| 4.4.3.3 | Tunnels/ Pressure Shafts | 179 |
| 4.4.3.4 | Balancing Reservoir | 180 |
| 4.4.3.5 | Fore Bay | 180 |
| 4.4.3.6 | Penstocks and Surge shaft | 180 |
| 4.4.3.7 | Surface power house (PH-II) | 182 |
| 4.5 | Upper Betwa Project components | 184 |
| 4.5.1 | Engineering Assessment of Makodia Dam | 184 |
| Para no. | Particulars | Page no. |
| 4.5.1.1 | General | 184 |
| 4.5.1.2 | Geology, Seismicity and Foundation | 184 |
| 4.5.1.3 | Alternative studies carried out for selection of sites and type of structures | 185 |
| 4.5.1.4 | Choice of final layout of all major components of the project and reason | 187 |
| 4.5.1.5 | Design flood and sedimentation studies | 188 |
| 4.5.1.6 | Free board | 188 |
| 4.5.1.7 | River Diversion arrangement | 189 |
| 4.5.1.8 | Construction materials | 190 |
| 4.5.1.9 | Details of model studies for important structures | 191 |
| 4.5.2 | Makodia dam | 191 |
| 4.5.2.1 | Makodia earth dam | 191 |
| 4.5.2.2 | Makodia concrete dam / non over flow section/ stability analysis/spillway section | 195 |
| 4.5.2.3 | Openings through Makodia dam | 198 |
| 4.6 | Barrages / Weirs | 199 |
| 4.6.1 | Barari Barrage | 199 |
| 4.6.1.1 | Sediment Data | 199 |
| 4.6.1.2 | Assumed Retrogression | 199 |
| 4.6.1.3 | Looseness Factor | 200 |
| 4.6.1.4 | Scour Depth | 200 |
| 4.6.1.5 | Intensity of discharge under design flood condition | 200 |
| 4.6.1.6 | Co-efficient of discharge | 200 |
| 4.6.1.7 | Exit Gradient value | 200 |
| 4.6.1.8 | Stresses Allowed | 200 |
| 4.6.1.9 | Type (Concrete/Masonry)/Profile cut off, upstream and down stream aprons, uplift pressure relief arrangements etc. | 201 |
| 4.6.1.10 | Gates, types of gates and hoist bridge and stop logs | 201 |
| 4.6.2 | Kesari barrage | 202 |
| 4.6.2.1 | Sediment data | 203 |
| 4.6.2.2 | Assumed retrogression | 203 |
| 4.6.2.3 | Looseness factor | 203 |
| 4.6.2.4 | Scour depth | 203 |
| 4.6.2.5 | Intensity of discharge under design flood condition | 203 |
| 4.6.2.6 | Co-efficient of discharge | 203 |
| 4.6.2.7 | Exit Gradient value | 203 |
| 4.6.2.8 | Stresses Allowed | 204 |
| 4.6.2.9 | Type (Concrete/Masonry)/Profile cut off, upstream and down stream aprons, uplift pressure relief arrangements etc. | 204 |
| 4.6.2.10 | Gates, types of gates and hoist bridge and stop logs | 204 |
| 4.6.3 | Canals of upper Betwa system | 205 |
| Para no. | Particulars | Page no. |
| 4.6.3.1 | Makodia dam canal system – Right Bank Canal | 206 |
| 4.6.3.2 | Study of integrated network of canal system and its operation to utilize the water potential of streams crossed by main canal system by provision of storage / tail tank etc. | 208 |
| 4.6.3.3 | Description of soil profile | 208 |
| 4.6.3.4 | Evaluation of design parameters, suggested treatment for problematic reaches. | 208 |
| 4.6.3.5 | Details of lining | 208 |
| 4.6.3.6 | Transmission losses | 209 |
| 4.6.3.7 | Cut off statement showing the details of the discharge required from tail to the head | 209 |
| 4.6.3.8 | Design calculation for adequacy of canal sections adopted | 209 |
| 4.6.3.9 | Design discharge data for each distributaries | 209 |
| 4.6.3.10 | Canal structures across Makodia right bank canal | 209 |
| 4.6.4 | Makodia dam – left bank canal | 211 |
| 4.6.5 | Barari barrage – Right bank canal | 214 |
| 4.6.6 | Kesari barrage – Right bank canal | 214 |
| 4.7 | Infrastructure studies | 214 |
| 4.8 | Industrial and urban use | 214 |
| 4.9 | Instrumentation | 215 |
| 4.10 | Navigation and Tourism development | 215 |
| 4.11 | Operation and maintenance | 215 |
| 4.12 | Other studies | 215 |
|  | Chapter-V : Reservoir & Power |  |
| 5.0 | General | 216 |
| 5.1 | Daudhan Reservoir | 216 |
| 5.1.1 | Fixation of storage and reservoir levels approach – criteria | 216 |
| 5.1.1.1 | Dead storage level(DSL) | 217 |
| 5.1.1.2 | Low water level/Minimum Draw Down level(MDDL) | 218 |
| 5.1.1.3 | Full reservoir level | 219 |
| 5.1.1.4 | Maximum water level(MWL) | 220 |
| 5.1.1.5 | Maximum backwater at Full reservoir level and maximum water and its effect points from the axis of the structure | 221 |
| 5.1.1.6 | Fetch | 221 |
| 5.1.1.7 | Direction of wind-velocity of wind – wave height – Free board- Top of dam | 221 |
| 5.1.2 | Sedimentation data and studies | 222 |
| 5.1.2.1 | Rate of sedimentation | 222 |
| 5.1.2.2 | Sedimentation fraction | 225 |
| 5.1.2.3 | Quantity of sediment | 225 |
| 5.1.2.4 | Types and shape of reservoir | 226 |
| Para no. | Particulars | Page no. |
| 5.1.2.5 | Sediment studies | 226 |
| 5.1.3 | Life of Reservoir in years with basis | 226 |
| 5.1.4 | Capacity | 226 |
| 5.1.4.1 | Capacities | 226 |
| 5.1.4.2 | Storage | 226 |
| 5.1.4.3 | Water tightness of the reservoir | 227 |
| 5.1.4.4 | Annual losses | 227 |
| 5.1.4.5 | Flood absorption | 227 |
| 5.1.5 | Effects on sub-soil water table in the adjoining areas particularly downstream of the dam | 228 |
| 5.1.6 | Reservoir rim stability | 228 |
| 5.1.7 | Area of submergence | 228 |
| 5.1.7.1 | Maximum water level | 228 |
| 5.1.7.2 | Full reservoir level | 228 |
| 5.1.7.3 | Submergence Ratio submerged (cultivated)area/CCA | 228 |
| 5.1.8 | Land acquisition-Property submerged-rehabilitation | 228 |
| 5.1.8.1 | Land acquisition | 228 |
| 5.1.8.2 | Details of property submerged | 229 |
| 5.1.8.3 | Rehabilitation of oustees | 229 |
| 5.1.9 | Recreation facilities | 230 |
| 5.1.10 | Pisciculture | 230 |
| 5.1.11 | Need and recommendation for soil conservation measure in the catchment | 230 |
| 5.1.12 | Any other relevant information | 231 |
| 5.2 | Makodia reservoir | 231 |
| 5.2.1 | Fixation of storage and reservoir levels approach – criteria | 231 |
| 5.2.1.1 | Dead storage level(DSL) | 232 |
| 5.2.1.2 | Low water level/Minimum Draw Down level(MDDL) | 232 |
| 5.2.1.3 | Full reservoir level | 232 |
| 5.2.1.4 | Maximum water level(MWL) | 233 |
| 5.2.1.5 | Maximum backwater at Full reservoir level and maximum water levels and its impacts, maximum distance of such points from the axis of the structure | 233 |
| 5.2.1.6 | Fetch | 233 |
| 5.2.1.7 | Direction of wind-velocity of wind – wave height – Free board- Top of dam | 234 |
| 5.2.2 | Sedimentation data and studies | 234 |
| 5.2.1.1 | Rate of sedimentation with basis | 234 |
| 5.2.2.2 | Sedimentation fraction | 236 |
| 5.2.2.3 | Quantity of sediment | 236 |
| 5.2.2.4 | Types and shape of reservoir | 236 |
| 5.2.2.5 | Sediment studies | 236 |
| Para no. | Particulars | Page no. |
| 5.2.2.6 | Sedimentation in the reservoir after 50 and 100 years | 237 |
| 5.2.3 | Life of Reservoir in years with basis | 237 |
| 5.2.4 | Capacity | 237 |
| 5.2.4.1 | Capacities | 237 |
| 5.2.4.2 | Storage | 237 |
| 5.2.4.3 | Water tightness of the reservoir | 237 |
| 5.2.4.4 | Annual losses | 237 |
| 5.2.4.5 | Flood absorption | 238 |
| 5.2.5 | Effects on sub-soil water table in the adjoining areas particularly downstream of the dam | 238 |
| 5.2.6 | Reservoir rim stability | 238 |
| 5.2.7 | Area of submergence | 238 |
| 5.2.7.1 | Maximum water level | 238 |
| 5.2.7.2 | Full reservoir level | 238 |
| 5.2.7.3 | Submergence Ratio submerged (cultivated)area/CCA | 238 |
| 5.2.8 | Land acquisition-Property submerged-rehabilitation | 239 |
| 5.2.8.1 | Land acquisition | 239 |
| 5.2.8.2 | Details of property submerged | 239 |
| 5.2.8.3 | Rehabilitation of oustees | 239 |
| 5.2.9 | Recreation facilities | 240 |
| 5.2.10 | Pisciculture | 240 |
| 5.2.11 | Need and recommendation for soil conservation measure in the catchment | 240 |
| 5.2.12 | Any other relevant information | 240 |
| 5.3 | Barari Barrage | 241 |
| 5.4 | Kesari Barrage | 241 |
| 5.5 | Power Potential & Benefits | 243 |
| 5.5.1 | Introduction | 243 |
| 5.5.1.1 | Present status of power development in State/region | 243 |
| 5.5.2 | Hydrology | 248 |
| 5.5.3 | Input data for the Power Potential Study | 249 |
| 5.5.3.1 | Hydrological flow data | 249 |
| 5.5.3.2 | Evaporation data | 249 |
| 5.5.3.4 | Tailrace water level(TWL) | 250 |
| 5.5.3.5 | Drinking Water & Irrigation Requirements | 250 |
| 5.5.3.6 | Full Reservoir Level(FRL) | 251 |
| 5.5.3.7 | Minimum Draw Down Level(MDDL) | 251 |
| 5.5.3.8 | Draw Down level for Power generation | 251 |
| 5.5.3.9 | Head Availability & head loss in Water Conductor system | 252 |
| 5.5.3.10 | Operation of the Power houses | 252 |
| 5.5.4 | Simulation Strategy | 253 |
| 5.5.5 | Results of the simulation study | 253 |
| Para no. | Particulars | Page no. |
| 5.5.5.2 | Installed Capacity & Unit size | 254 |
| 5.5.5.2.1 | Daudhan power house | 254 |
| 5.5.5.2.2 | Lower level tunnel power house | 255 |
| 5.5.6 | Graphical analysis of Simulation study | 258 |
| 5.5.7 | Adequacy pondage at Gangau weir | 260 |
| 5.5.8 | Impact of flows in the final scenario | 260 |
| 5.5.9 | Pumping Requirement for Ken-Betwa Link canal | 261 |
| 5.5.10 | Summary of the Study | 261 |
| 5.6 | Electro-mechanical equipments | 263 |
| 5.6.1 | Introduction | 263 |
| 5.6.2 | Transportation constraints | 264 |
| 5.6.3 | Broad Scope of Works | 264 |
| 5.6.3.1 | Power house-I | 264 |
| 5.6.3.2 | Power house-II | 266 |
| 5.6.4 | Selection of Parameters of Main Generating units & Associated equipment | 267 |
| 5.6.5 | Electro-Mechanical equipment | 269 |
| 5.6.5.1 | Turbines-Construction aspects | 269 |
| 5.6.5.2 | Governing Equipment | 270 |
| 5.6.5.3 | Main Inlet Valve | 270 |
| 5.6.5.4 | Oil Pressure system for Governor and Turbine inlet valves | 271 |
| 5.6.6 | Generator | 271 |
| 5.6.7 | Excitation system for Generator | 274 |
| 5.6.7.1 | For Power house-I | 274 |
| 5.6.7.2 | For Power house-II | 275 |
| 5.6.8 | Control & Monitoring system | 276 |
| 5.6.9 | 11 KV Bus Duct | 277 |
| 5.6.10 | Generator, Transformer & other Transformers | 278 |
| 5.6.11 | 132 KV Switchyard (Power house-I) | 279 |
| 5.6.12 | 33 KV Switchyard (Power house-II) | 280 |
| 5.6.13 | Fencing | 281 |
| 5.6.14 | Power Evacuation | 281 |
| 5.6.15 | Relay & Protection system (Power house-I & II) | 281 |
| 5.6.16 | Auxiliary Equipment / System | 286 |
| 5.6.17 | Construction Power | 294 |
| 5.6.18 | Estimates for Electrical & Mechanical works | 294 |
| 5.6.19 | Drawings | 294 |

List of Annexures

| Annexure no. | Particulars | Page no. |
| --- | --- | --- |
| 1.1 | Concurrence letter of U.P. State Government | 297 |
| 1.2 | Concurrence letter of M.P.State Government | 298 |
| 1.3 | MoU Among the state of M.P., state of U.P. and Union Govt. on Ken-Betwa Project Link | 300 |
| 1.4 | Minutes of third co-ordination committee | 304 |
| 1.5 | List of projects in Upper Betwa region | 307 |
| 1.6 (a) | Composition of Hydrological committee | 309 |
| 1.6 (b) | Composition of revised Hydrological committee | 311 |
| 1.7 (a) | Composition of committee for award, monitoring & evaluation in regard to Socio-economic & Environmental Studies of DPR of Ken – Betwa link project | 312 |
| 1.7 (b) | Revised Composition of Committee for award, monitoring & evaluation in regard to Socio- economic & Environmental Studies of DPR of Ken – Betwa link project | 314 |
| 1.7 (c) | Reconstitution of Committee for award, monitoring & evaluation in regard to Socio-economic & Environmental Studies of DPR of Ken – Betwa link project | 316 |
| 1.8 | Constitution of committee to monitor and supervise the overall work of preparation of DPR of Ken-Betwa link project | 318 |
| 1.9 | Constitution of Steering Committee for Ken-Betwa link project | 321 |
| 1.10 | Permission letter from MoEF for carrying out surveys in Non Park area | 322 |
| 1.11(a)&(b) | Permission letter from MoEF for carrying out surveys in Park area | 324 |
| 2.1 | Details of Permanent BM established near Daudhan Dam & along the Ken-Betwa link canal | 328 |
| 2.2 | Details of cross-drainage/masonry structures across K-B Link canal | 330 |
| 2.3.1 | Enquiry about Ancient monuments from ASI | 332 |
| 2.3.2 | Information about mines and minerals enroute of K-B Link from Assistant Minerals officers, Chhatarpur.(M.P) | 333 |
| 2.3.3 | Information about mines and minerals under submergence of Daudhan dam and enroute of K-B Link from Minerals officer, Panna | 334 |
| 2.4 | Summarized details of drill hole logs across Daudhan Dam axis | 335 |
| Annexure no. | Particulars | Page no. |
| 2.5 | List of raingauge station in Ken basin and their period of availability | 337 |
| 2.6 | Details of PBM’s established at Upper Betwa Projects | 338 |
| 2.7 | Details of cross-Drainage / Masonry structures across Right Bank Canal of Makodia dam | 339 |
| 2.8 | Details of cross-Drainage / Masonry structures across Left Bank Canal of Makodia dam | 341 |
| 2.9 | Summarised details of exploratory drill holes of Makodia dam axis | 342 |
| 2.10 | List of raingauge stations (IMD) in Upper Betwa sub-basin and their period of data availability | 343 |
| 2.11 | Details of cross-Drainage / Masonry structures across Right Bank Canal of Kesari Barrage | 344 |
| 4.1 | Co-ordinates of Probable maximum flood hydrograph at Daudhan dam site | 345 |
| 4.2 | Original and revised (after 50 and 100 year) Elevation – Area – Capacity values for Daudhan reservoir | 346 |
| 4.3 | Computation of transmission losses in the Ken-Betwa link canal | 347 |
| 4.4.1 | Design of link canal section (Reach – 1) | 349 |
| 4.4.2 | Design of link canal section (Reach – 2) | 350 |
| 4.4.3 | Design of link canal section (Reach – 3) | 351 |
| 4.4.4 | Design of link canal section (Reach – 4) | 352 |
| 4.5 | Details of distributaries offtaking from Ken-Betwa link canal | 353 |
| 4.6 | Design of Cross Regulator | 354 |
| 4.7 | Design of Exit Regulator at end | 356 |
| 4.8 | List of C.D. Structures across Ken-Betwa link canal | 357 |
| 4.9 | Design of canal siphon across Dhasan river | 358 |
| 4.10 | List of cross masonry works across the Ken-Betwa link canal | 364 |
| 4.11 | Original and revised (after 50 and 100 years) Elevation – Area – Capacity values for Makodia reservoir | 365 |
| 4.12 | Design of Barari Barrage | 366 |
| 4.13 | Design of Kesari Barrage | 368 |
| 4.14.1 | Design of Makodia RBC section (Reach – 1) | 371 |
| 4.14.2 | Design of Makodia RBC section (Reach – 2) | 372 |
| 4.14.3 | Design of Makodia RBC section (Reach – 3) | 373 |
| 4.14.4 | Design of Makodia RBC section (Reach – 4) | 374 |
| 4.14.5 | Design of Makodia RBC section (Reach – 5) | 375 |
| 4.15 | Details of distributaries offtaking from Makodia RBC | 376 |
| Annexure no. | Particulars | Page no. |
| 4.16 | List of C.D. / C.M. structures across Makodia RBC | 377 |
| 5.1.1 | Water Availability and surplus of Ken basin upto Daudhan dam site | 379 |
| 5.1.2 | Results of simulation studies at Daudhan dam site | 380 |
| 5.1.3 (1/2) | Assessment of sediment deposition after 50 year by Empirical area reduction method (Daudhan) | 381 |
| 5.1.3 (2/2) | Assessment of sediment deposition after 100 year by Empirical area reduction method (Daudhan) | 382 |
| 5.1.4(1/2) | Reservoir routing (Modified puls method) for Daudhan when 30 gates are operational | 383 |
| 5.1.4(2/2) | Reservoir routing (Modified puls method) for Daudhan when 29 gates are operational | 384 |
| 5.1.5 | A geotechnical report on reservoir competency of the Daudhan dam, Ken Betwa link project, Chhatarpur and Panna districts, M.P. | 385 |
| 5.2.1 | Water availability and surplus upto Makodia dam, Barari and Kesari Barrage sites | 396 |
| 5.2.2 | Reliabilities of the Upper Betwa Projects in meeting the demands | 397 |
| 5.2.3 (1/2) | Assessment of sediment deposition after 100 year by Empirical area reduction method (Makodia dam) | 398 |
| 5.2.3(2/2) | Assessment of sediment deposition after 10year by Empirical area reduction method (Makodia dam) | 399 |
| 5.2.4 | Reservoir routing (Modified Puls Method) for Makodia dam | 400 |
| 5.2.5 | A geotechnical report on reservoir competency of the Makodia dam, Ken Betwa link project, Raisen district, M.P. | 401 |
| 5.5.1 | Availability of Gross Head at Daudhan power house for power generation | 408 |
| 5.5.2 | Head loss at Daudhan power house for Power Generation | 409 |
| 5.5.3 | Available net head at Daudhan power house for Power Generation | 410 |
| 5.5.4 | Turbine output capability factor- Daudhan | 411 |
| 5.5.5 | Unrestricted power output at Daudhan power house considering turbine capability | 412 |
| 5.5.6 | Unrestricted energy generation at Daudhan power house considering turbine capability | 413 |
| 5.5.7 | Power generation at Daudhan power house with IC 60 MW | 414 |
| 5.5.8 | Energy generation at Daudhan Power house with IC 60 MW | 415 |
| Annexure no. | Particulars | Page no. |
| 5.5.9 | Monthwise flows available at Lower Level Tunnel Power House for generation | 416 |
| 5.5.10 | Available gross head at Lower Level tunnel power house for power generation | 417 |
| 5.5.11 | Head loss at Lower level Tunnel power house for power generation | 418 |
| 5.5.12 | Available net head at Lower Level Tunnel power house for power generation | 419 |
| 5.5.13 | Turbine output capability factor – Lower Level Tunnel Power House | 420 |
| 5.5.14 | Unrestricted Power Output at Lower Level Tunnel Power House | 421 |
| 5.5.15 | Unrestricted energy generation at Lower Level Tunnel Power House with turbine capability considered | 422 |
| 5.5.16 | Power generation at Lower level Tunnel Power House with IC 18 MW | 423 |
| 5.6.1 | Abstract of Cost of Electro-Mechanical works for Power House –I (2x30 MW) | 424 |
| 5.6.1.1 | Preliminary | 425 |
| 5.6.1.2 | Generator, turbine & accessories | 426 |
| 5.6.1.3 | Auxiliary electrical equipment for power station | 427 |
| 5.6.1.4 | Auxiliary mechanical equipment and services for power station | 428 |
| 5.6.1.5 | Sub station equipment and auxiliary equipment & service for the switchyard | 429 |
| 5.6.2 | Abstract of Cost of Electro-Mechanical works for Power House –II (3 x 6 MW) | 430 |
| 5.6.2.1 | Preliminary | 431 |
| 5.6.2.2 | Generator, turbine & accessories | 432 |
| 5.6.2.3 | Auxiliary electrical equipment for power station | 433 |
| 5.6.2.4 | Auxiliary mechanical equipment and services for power station | 434 |
| 5.6.2.5 | Sub station equipment and auxiliary equipment & service for the switchyard | 435 |
|  | Abbreviations used |  |

Report Volume - II

| Para no. | Particulars | Page no. |
| --- | --- | --- |
|  | Chapter-VI : Irrigation Planning and Command Area Development |  |
| 6.1 | Existing/proposed irrigation facilities in the proposed project command area | 436 |
| 6.1.1 | Enroute command | 436 |
| 6.1.2 | Ken command in M.P | 437 |
| 6.1.3 | Ken command in U.P | 437 |
| 6.1.4 | Upper Betwa command | 438 |
| 6.2 | Existing cropping pattern | 438 |
| 6.2.1 | Existing area under rain-fed cultivation | 438 |
| 6.2.1.1 | Enroute command | 438 |
| 6.2.1.2 | Ken command(M.P.) | 439 |
| 6.2.1.3 | Ken command(U.P.) | 440 |
| 6.2.1.4 | Upper Betwa command | 440 |
| 6.2.1.5 | Rainfall during monsoon (max, min. & normal rainfall) | 440 |
| 6.2.1.6 | Rainfall during non-monsoon (max, min. & normal rainfall) | 441 |
| 6.3 | Soil surveys | 441 |
| 6.3.1 | Soil capability classification | 441 |
| 6.3.2 | Land irrigability classification | 441 |
| 6.4 | Proposed cropping pattern | 441 |
| 6.4.1 | Proposed Irrigation facilities | 444 |
| 6.4.1.1 | Enroute command | 444 |
| 6.4.1.2 | Ken command (M.P) | 444 |
| 6.4.1.3 | Upper Betwa command | 444 |
| 6.4.2 | Scope for double and multiple cropping pattern and change in cropping pattern on the basis of latest available data | 444 |
| 6.4.2.1 | Soils | 445 |
| 6.4.2.2 | Agro-climatic conditions | 445 |
| 6.4.2.3 | Water and other inputs like seeds, fertilizers, etc. | 445 |
| 6.4.2.4 | Irrigated crops in the adjoining areas | 445 |
| 6.4.2.5 | Attitude of farmers towards modern irrigated agricultural practices | 445 |
| 6.5 | Crop water requirement | 446 |
| 6.6 | Water planning | 448 |
| 6.6.1 | Surface water | 448 |
| 6.6.1.1 | Demand table of the project | 448 |
| 6.6.1.2 | Designed head discharge of canal systems | 453 |
| 6.6.2 | Ground water | 453 |
| 6.6.2.1 | Ground water quality | 453 |
| Para no. | Particulars | Page no. |
| 6.6.2.2 | Conjunctive use/Ground water support | 454 |
| 6.7 | Command area | 454 |
| 6.8 | Command area development | 454 |
| 6.8.1 | Details of enroute command | 454 |
| 6.8.1.1 | Location | 454 |
| 6.8.1.2 | Classification of land (forest, grass land, cultivable land, cultivable waste, barren land) | 455 |
| 6.8.1.3 | Size of land holding | 456 |
| 6.8.1.4 | Climate | 457 |
| 6.8.1.5 | Irrigation | 457 |
| 6.8.1.6 | Socio-economic aspects | 458 |
| 6.8.1.7 | Infrastructure facilities | 459 |
| 6.8.1.8 | Topography and soils | 461 |
| 6.8.1.9 | Ground water and drainage | 461 |
| 6.8.1.10 | Agriculture | 462 |
| 6.8.1.11 | Farmer’s attitude towards improved agricultural practices | 462 |
| 6.8.1.12 | Identification of problems in enroute command area | 463 |
| 6.8.1.13 | Financial problems | 463 |
| 6.8.1.14 | Proposed cropping pattern, with justification based on land irrigability classification, agroclimatic conditions developed irrigated cropping pattern in adjoining project/area, etc. | 464 |
| 6.8.1.15 | Land development work proposals | 464 |
| 6.8.1.16 | Ayacut roads | 464 |
| 6.8.1.17 | Benefits | 464 |
| 6.8.2 | Details of Upper Betwa command | 466 |
| 6.8.2.1 | Command area details | 466 |
| 6.8.2.2 | Classification of land (forest, grass land, cultivable land, cultivable waste, barren land) | 467 |
| 6.8.2.3 | Size of land holding | 467 |
| 6.8.2.4 | Climate of the command area | 467 |
| 6.8.2.5 | Irrigation | 468 |
| 6.8.2.6 | Socio-economic aspects | 469 |
| 6.8.2.7 | Infrastructure facilities | 469 |
| 6.8.2.8 | Topography and soils | 470 |
| 6.8.2.9 | Ground water and drainage | 470 |
| 6.8.2.10 | Agriculture | 470 |
| 6.8.2.11 | Farmer’s attitude towards improved agricultural practices | 471 |
| 6.8.2.12 | Identification of problems in command area | 471 |
| 6.8.2.13 | Financial problems | 472 |
| Para no. | Particulars | Page no. |
| 6.8.2.14 | Proposed cropping pattern, with justification based on land irrigability classification, agroclimatic conditions developed irrigated cropping pattern in adjoining project/area, etc. | 472 |
| 6.8.2.15 | Land development work proposals | 472 |
| 6.8.2.16 | Ayacut roads | 473 |
| 6.8.2.17 | Benefits | 473 |
| 6.8.3 | Details of Ken command | 474 |
| 6.8.3.1 | Location | 474 |
| 6.8.3.2 | Classification of land (forest, grass land, cultivable land, cultivable waste, barren land) | 474 |
| 6.8.3.3 | Size of land holding | 475 |
| 6.8.3.4 | Climate | 475 |
| 6.8.3.5 | Irrigation | 477 |
| 6.8.3.6 | Socio-economic aspects | 478 |
| 6.8.3.7 | Infrastructure facilities | 478 |
| 6.8.3.8 | Topography and soils | 479 |
| 6.8.3.9 | Ground water and drainage | 479 |
| 6.8.3.10 | Agriculture | 480 |
| 6.8.3.11 | Farmer’s attitude towards improved agricultural practices | 480 |
| 6.8.3.12 | Identification of problems in command area | 481 |
| 6.8.3.13 | Financial problems | 481 |
| 6.8.3.14 | Proposed cropping pattern, with justification based on land irrigability classification, agroclimatic conditions developed irrigated cropping pattern in adjoining project/area, etc. | 481 |
| 6.8.3.15 | Land development work proposals | 482 |
| 6.8.3.16 | Ayacut roads | 482 |
| 6.8.3.17 | Benefits | 482 |
|  | Chapter-VII : Construction Program, Man Power Deployment and Plant Planning |  |
| 7.1 | General | 484 |
| 7.2 | Main project components | 484 |
| 7.2.1 | Salient features of main components of the project | 485 |
| 7.3 | Basis for study | 486 |
| 7.3.1 | General | 486 |
| 7.3.2 | Construction Material sources | 486 |
| 7.3.3 | Basic considerations | 487 |
| 7.3.3.1 | Scheduled working hours | 487 |
| 7.3.3.2 | Construction Period | 488 |
| 7.4 | Construction Methodology and Equipment | 489 |
| 7.4.1 | River Diversion works | 489 |
| Para no. | Particulars | Page no. |
| 7.4.2 | Earth fill dam(Daudhan) | 489 |
| 7.4.2.1 | Surface Excavation | 490 |
| 7.4.2.2 | Fill Placement | 491 |
| 7.4.2.3 | List of Major construction plant and equipment for earth dam | 495 |
| 7.4.2.4 | Construction Programme | 496 |
| 7.4.3 | Concrete dam(Daudhan) | 497 |
| 7.4.3.1 | Surface Excavations | 497 |
| 7.4.3.2 | Concreting | 498 |
| 7.4.3.3 | List of Major construction plant and equipment for concrete dam | 499 |
| 7.4.3.4 | Construction Programme | 500 |
| 7.4.4 | Power house-I (Dam power house) complex | 500 |
| 7.4.4.1 | Excavation and concreting | 500 |
| 7.4.4.2 | List of Major Construction Plant and Equipment for Powerhouse-I | 501 |
| 7.4.4.3 | Construction Programme | 501 |
| 7.4.5 | Power house-II (Canal Power house) complex | 501 |
| 7.4.5.1 | Intake structure for canal power house (Lower level tunnel) | 502 |
| 7.4.5.2 | Surge shaft | 503 |
| 7.4.5.3 | Power house-II (Canal Power house) | 505 |
| 7.4.5.4 | List of Major construction Plant and Equipment for Power house-II complex | 506 |
| 7.4.5.5 | Construction Programme | 506 |
| 7.4.6 | Ken Left Bank Canal | 507 |
| 7.4.6.1 | List of Major construction plant and equipment for Ken LBC | 508 |
| 7.4.6.2 | Construction Programme | 509 |
| 7.4.7 | Ken-Betwa link canal | 509 |
| 7.4.7.1 | Upper Level Tunnel | 509 |
| 7.4.7.2 | Link Canal | 509 |
| 7.4.7.3 | List of Major Construction Plant and Equipment for Ken-Betwa Link Canal | 511 |
| 7.4.7.4 | Construction Programme | 512 |
| 7.4.8 | Upper Betwa Projects | 512 |
| 7.4.8.1 | Earthfill dam(Makodia) | 512 |
| 7.4.8.1.1 | Surface Excavation | 513 |
| 7.4.8.1.2 | Fill Placement | 513 |
| 7.4.8.2 | Kesari & Barari Barrages | 514 |
| 7.4.8.2.1 | Surface Excavation | 515 |
| 7.4.8.2.2 | Concreting | 515 |
| 7.4.8.3 | Concrete Dam (Makodia) | 515 |
| 7.4.8.3.1 | Surface Excavation | 516 |
| 7.4.8.3.2 | Concreting | 516 |
| 7.4.8.4 | Upper Betwa Canals | 517 |
| Para no. | Particulars | Page no. |
| 7.4.8.4.1 | List of Major Construction Plant and Equipment for Upper Betwa projects | 518 |
| 7.4.8.4.2 | Construction Programme | 518 |
| 7.5 | Deployment schedule | 519 |
| 7.6 | Total Requirement of Major Construction Equipment | 520 |
| 7.7. | Organisation set up | 520 |
| 7.8 | General Purpose Equipment and Inspection Vehicles | 521 |
| 7.9 | Year wise allocation of cost | 521 |
|  | Chapter-VIII : Environment Impact Assessment And Environment Management Plan |  |
| 8.1 | The proposed project | 522 |
| 8.1.1 | Project background | 522 |
| 8.1.2 | Project justification | 523 |
| 8.1.3 | Project description | 523 |
| 8.2 | Site selection | 524 |
| 8.2.1 | Alternate site | 524 |
| 8.2.2 | No project option | 525 |
| 8.3 | Legal status of the project | 525 |
| 8.4 | Baseline environmental data | 526 |
| 8.4.1 | Air Quality | 526 |
| 8.4.1.1 | Meteorology | 526 |
| 8.4.2 | Water Quality | 527 |
| 8.4.2.1 | Surface Water Quality | 527 |
| 8.4.2.2 | Ground Water Quality | 529 |
| 8.4.2.3 | Ground Water levels | 530 |
| 8.4.2.4 | Depth to water level | 530 |
| 8.4.2.5 | Ground water level fluctuations | 531 |
| 8.4.2.6 | Ground water assessment | 532 |
| 8.4.3 | Land environment | 532 |
| 8.4.3.1 | Land use | 532 |
| 8.4.3.2 | Mineral Resources | 533 |
| 8.4.3.3 | Geology | 534 |
| 8.4.3.4 | Soils | 534 |
| 8.4.4 | Public Health | 535 |
| 8.4.4.1 | Sanitation | 536 |
| 8.4.4.2 | Drinking water supply | 536 |
| 8.4.4.3 | Water Borne and communicable diseases | 536 |
| 8.4.4.4 | Nutrition | 537 |
| 8.4.4.5 | Construction Phase | 537 |
| 8.4.4.6 | Post Construction Phase | 537 |
| Para no. | Particulars | Page no. |
| 8.4.5 | Biological(Terrestrial and Aquatic) environment | 537 |
| 8.4.5.1 | Flora of the project area | 538 |
| 8.4.5.2 | Non-wood forest products | 538 |
| 8.4.5.3 | Medicinal Plants | 538 |
| 8.4.5.4 | Physiognomy and indices of diversity | 539 |
| 8.4.5.5 | Orchids and other species of the Ken-Betwa catchment area | 539 |
| 8.4.5.6 | Status of the fauna | 539 |
| 8.4.5.7 | Fish fauna of Ken and Betwa rivers | 540 |
| 8.4.5.8 | Other fauna of the Ken-Betwa catchment and command areas | 540 |
| 8.5 | Environmental Impact Assessment | 540 |
| 8.5.1 | Impact on Air Environment | 540 |
| 8.5.1.1 | Noise Environment | 541 |
| 8.5.1.2 | Air Environment | 541 |
| 8.5.2 | Impact on Water Environment | 542 |
| 8.5.2.1 | Flood studies and flood routing | 542 |
| 8.5.2.2 | Siltation | 543 |
| 8.5.2.3 | Acidification of lakes and water bodies | 543 |
| 8.5.3 | Impact on water quality(Surface water) | 543 |
| 8.5.3.1 | Construction phase | 543 |
| 8.5.3.2 | Operation phase | 544 |
| 8.5.4 | Impact on water Quality(Ground Water) | 545 |
| 8.5.4.1 | Impact due to change in waste assimilation capacity of the river system | 545 |
| 8.5.4.2 | Impact on Drainage system | 546 |
| 8.5.4.3 | Impact due to Contamination by Agro-chemicals and Fertilizers | 546 |
| 8.5.5 | Impact on Land Environment | 546 |
| 8.5.5.1 | Impact on Land use | 547 |
| 8.5.5.2 | Roads | 547 |
| 8.5.5.3 | Muck Generation | 548 |
| 8.5.5.4 | Submergence of Land | 548 |
| 8.5.5.5 | Increase in food grain production | 548 |
| 8.5.5.6 | Land degradation | 548 |
| 8.5.5.7 | Reservoir Induced Seismicity | 549 |
| 8.5.5.8 | Recharge of ground water | 549 |
| 8.5.5.9 | Water logging and Salinization | 549 |
| 8.5.5.10 | Impact on Soil Erosion | 549 |
| 8.5.6 | Impact on Bio-diversity | 550 |
| 8.5.6.1 | Impact on Biota | 550 |
| 8.5.6.2 | Impact on Habitat loss | 550 |
| 8.5.6.3 | Impact due to Habitat change | 550 |
| 8.5.6.4 | Impact on the breeding grounds | 551 |
| Para no. | Particulars | Page no. |
| 8.5.6.5 | Impact on Animals | 551 |
| 8.5.6.6 | Impact on Aquatic Environment | 551 |
| 8.5.6.7 | Impact on Sensitive Eco-system | 551 |
| 8.5.6.8 | Impact due to Bioaccumulation and Biomagnifications | 552 |
| 8.5.6.9 | Impact due to change in Ecological functioning of river system | 552 |
| 8.5.6.10 | Impact on Growth of Aquatic weeds | 552 |
| 8.5.6.11 | Impacts on Fish Spawning and Migration | 552 |
| 8.6 | Environmental Management Plan | 553 |
| 8.6.1 | Air Quality | 553 |
| 8.6.2 | Water Quality | 553 |
| 8.6.2.1 | Surface water | 554 |
| 8.6.2.2 | Ground water | 554 |
| 8.6.3 | Land Management Plan | 554 |
| 8.6.3.1 | Land Management | 555 |
| 8.6.3.2 | Restoration Plan for Quarry sites | 555 |
| 8.6.3.3 | Silt Transfer | 555 |
| 8.6.3.4 | Land Scaping of Project Sites | 556 |
| 8.6.3.5 | Catchment Area Treatment | 556 |
| 8.6.3.6 | Conservation and Management Measures | 557 |
| 8.6.3.7 | Command Area Management | 558 |
| 8.6.4 | Public Health | 558 |
| 8.6.4.1. | Preventive and Curative Measures | 558 |
| 8.6.4.2 | Sewage waste disposal | 559 |
| 8.6.4.3 | AIDS control | 559 |
| 8.6.5 | Bio Diversity Management Plan | 559 |
| 8.6.5.1 | Identification of Areas and Habitats that need conservation | 559 |
| 8.6.5.2 | Management Plan | 560 |
| 8.6.6 | Disaster Management | 561 |
| 8.6.7 | The EMP costs | 561 |
|  | Chapter- IX : Socio-Economic Aspects and R & R |  |
| 9.1 | Socio-economic Aspects | 562 |
| 9.1.1 | Demography | 562 |
| 9.1.2 | Agriculture | 563 |
| 9.1.3 | Literacy | 563 |
| 9.1.4 | Public Health Facilities | 564 |
| 9.1.5 | Submergence Area | 565 |
| 9.2 | Project Affected Villages | 565 |
| 9.2.1 | Livestock | 566 |
| 9.2.2 | Agricultural Implements | 566 |
| 9.2.3 | Income and Expenditure | 566 |
| Para no. | Particulars | Page no. |
| 9.2.4 | Housing | 567 |
| 9.3 | Project Affected Families | 567 |
| 9.4 | Resettlement and Economic Rehabilitation Plan | 569 |
| 9.4.1 | Identified PAFs | 569 |
| 9.4.2 | The Cost | 570 |
| 9.4.2.1 | Land Acquisition | 570 |
| 9.4.2.2 | Resettlement and Economic Rehabilitation of Displaced persons | 571 |
| 9.4.2.3 | Compensation in lieu of properties | 571 |
| 9.5 | Training | 571 |
| 9.5.1 | Training at Departmental level | 571 |
| 9.5.2 | Training the Project Affected Persons | 572 |
| 9.6 | Organisation and Management | 572 |
| 9.7 | Monitoring and Evaluation | 573 |
| 9.8 | Project Cost | 573 |
|  | Chapter-X : Cost Estimate, B C Ratio & Financial Aspects |  |
| 10.0 | General | 575 |
| 10.1 | Classification of Units | 575 |
| 10.1.1 | Unit-I: Head works | 576 |
| 10.1.1.1. | A-Direct Charges | 577 |
| 10.1.1.2 | B-Indirect Charges | 581 |
| 10.1.2 | Unit-II: Canals | 581 |
| 10.1.2.1 | A-Direct Charges | 582 |
| 10.1.2.2 | B-Indirect Charges | 588 |
| 10.1.3 | Unit-III: Hydroelectric Installation | 588 |
| 10.1.3.1 | A- Direct Charges | 589 |
| 10.1.3.2 | B- Indirect Charges | 591 |
| 10.1.4 | Unit-IV: Navigation works | 591 |
| 10.1.5 | Unit-V: Water Supply Works | 592 |
| 10.1.6 | Unit-VI: Command Area Development | 592 |
| 10.2 | Revenues | 592 |
| 10.2.1 | Yearly Programme of development w.r.t date of starting of construction of the project | 592 |
| 10.2.2. | Sources of Revenue | 592 |
| 10.2.2.1 | Water rates – Irrigation cess | 593 |
| 10.2.2.2 | Auction of Ferry service, inundated land lease auction for fruit bearing trees along canals, lease of land for shops in colony area, navigational permits | 594 |
| 10.2.2.3 | Power rate | 594 |
| 10.2.2.4 | Navigation | 594 |
| Para no. | Particulars | Page no. |
| 10.2.2.5 | Other sources (Pisciculture, tourism, etc.) | 594 |
| 10.2.3 | Concession in water rates(irrigation), Cargo and passenger rates, etc. | 594 |
| 10.2.4 | Administrative charges for supply of water and collection of revenues, etc. | 594 |
| 10.2.5 | If the area to be irrigated is prone to scarcity, the expenditure normally incurred to redress the scarcity | 595 |
| 10.2.6 | Year in which the revenue would start accruing from various sources counting from the first year of construction | 595 |
| 10.2.7 | Total income from various sources indicated | 595 |
| 10.2.8 | Details of staff proposed for collection of revenues and its basis | 595 |
| 10.2.9 | Net revenue expected from difference components of project | 595 |
| 10.2.10 | Productivity of project in terms of percentage financial returns | 596 |
| 10.3 | Benefit-Cost Ratio and Internal Rate of Return | 597 |
| 10.3.1 | Multipurpose projects | 597 |
| 10.3.1.1 | Allocation of cost | 597 |
| 10.3.1.2 | Estimate of annual cost | 597 |
| 10.3.1.3 | Benefit cost ratio | 598 |
| 10.3.1.4 | Internal rate of return | 598 |
| 10.3.1.5 | BC ratio for flood control component of the project | 598 |
| 10.3.2 | Benefits other than those considered in the BC ratio and IRR | 598 |
|  | Chapter-XI : Project Operation Philosophy |  |
| 11.1 | Concept of Interlinking of River | 599 |
| 11.2 | Some unfounded concerns about the project | 599 |
| 11.3 | The Project | 600 |
| 11.4 | Project in Construction Stage | 601 |
| 11.5 | Project in Operation Stage | 601 |
| 11.5.1 | Irrigation to get priority over power generation | 602 |
| 11.5.1.1 | Ken Command to be given First Priority | 602 |
| 11.5.1.2 | Enroute command to be given Second Priority | 602 |
| 11.5.1.3 | Upper Betwa Projects | 603 |
| 11.5.2 | Power | 603 |
| 11.5.3 | Drinking Water | 603 |
| 11.5.4 | Flood Control | 604 |
| 11.6 | Project in Maintenance Stage | 604 |
|  | Chapter – XII : Other Aspects |  |
| 12.1 | Foreign exchange element | 606 |
| 12.2 | Revenue | 606 |
| 12.2.1 | Irrigation water rates | 606 |
| Para no. | Particulars | Page no. |
| 12.2.2 | Betterment levy | 606 |
| 12.2.3 | Sale of Power | 607 |
| 12.3 | Financial resources | 607 |
| 12.4 | Future utilization of facilities(Buildings) | 607 |
| 12.5 | Legal aspects of interbasin transfers such as impact on existing Awards/Agreements/Treaties | 608 |
| 12.5.1 | Existing Interstate agreement on sharing of Ken water | 608 |
| 12.5.2 | Proposed water sharing of Ken basin upto Daudhan dam as per MOU | 608 |
| 12.6 | Public awareness programme | 610 |

List of Annexures

| Annexureno. | Particulars | Page no. |
| --- | --- | --- |
| 6.1(a) | Land irrigability classification of Ken command | 611 |
| 6.1(b) | Land irrigability classification of Enroute command | 613 |
| 6.1(c) | Land irrigability classification of Upper Betwa projects command | 614 |
| 6.1(d) | Land capability classification of Ken command | 616 |
| 6.1(e) | Land capability classification of Enroute command | 618 |
| 6.1(f) | Land capability classification of Upper Betwa projects command | 619 |
| 6.2 | Irrigation demand for different commands | 621 |
| 6.3 | Table showing total utilizable /extractable Groundwater availability and net draft in Ken command area in pre- project & Post project scenario | 623 |
| 6.4 | Table showing total utilizable /extractable Groundwater availability and net draft in enroute command area in pre- project & Post project scenario | 625 |
| 6.5 | Table showing total utilizable /extractable Groundwater availability and net draft in Upper Betwa command area in pre-project & Post project scenario | 627 |
| 7.1 | Construction Schedule | 629 |
| 7.2 | Deployment schedule of major construction equipments | 632 |
| 7.3 | List of Major construction Equipment | 634 |
| 7.4 | Organisational Chart | 636 |
| 7.5 | Man power requirement | 637 |
| 7.6 | Requirement of staff (other than field staff) | 638 |
| 7.7 | Requirement of field staff | 639 |
| 7.8 | Requirement of fund for the scheme and its yearly phasing | 640 |
| 8.1 | Abstract of cost of Environmental Management Plan | 643 |
| 9.1 | Total cost of R & R for project affected families economic rehabilitation plan | 645 |
| 10 | General Abstract of cost | 649 |
| 10.1 | General Abstract of Unit-I Head Works(Daudhan dam) | 652 |
| 10.2 | General Abstract of Unit-I Head Works (Upper Betwa projects) | 653 |
| 10.3 | General Abstract of Unit-II Canal system(Ken-Betwa link canal) | 654 |
| 10.4 | General Abstract of Unit-II Canal (Ken LBC system) | 655 |
| 10.5 | General Abstract of Unit-II Upper Betwa canal system | 656 |
| 10.6 | General Abstract of Unit-III Power(PH-I) | 657 |
| 10.7 | General Abstract of Unit-III Power(PH-II) | 658 |
| 10.8 | Unit-VI Command area development | 659 |
| 10.9 | Net Annual benefits from project | 660 |
| 10.9.1 | Gross value of produce in K-B Link canal command | 662 |
| 10.9.2 | Gross value of produce in Ken LBC command | 663 |
| Annexureno. | Particulars | Page no. |
| 10.9.3 | Gross value of produce in Upper Betwa projects command | 664 |
| 10.9.4 | Expenses on produce for K-B link canal command | 665 |
| 10.9.5 | Expenses on produce for Ken LBC command | 666 |
| 10.9.6 | Expenses on produce for Upper Betwa project command | 668 |
| 10.10 | Cost allocation | 669 |
| 10.11 | Calculation of Benefit Cost Ratio | 670 |
| 10.12 | Computation of Internal Rate of Return | 671 |
| 11.1 | Lr. No./Bodhi/HYD/98-Y/08 dated 01.08.08 of Water Resources Department of Government of Madhya Pradesh for proposal of projects in Upper Betwa sub-basin utilizing 190 MCM of delivered water in Betwa river | 674 |
| 11.2 | Lr no.3222346/IFC/08 dated 25.10.08 of Water Resources Department of Government of Madhya Pradesh for utilizing the remaining water delivered in Betwa river | 676 |
| 11.3 | Final Demand Table for the Reservoir at Daudhan | 677 |
| 11.4 | Water demand table for Upper Betwa Projects | 678 |
| 12.1 | Requirement of fund for the scheme and its yearly phasing | 679 |
|  | List of Abbreviations |  |

Appendix Volume-I: Survey & Investigations

| Appendix no. | Particulars | Page nos. |
| --- | --- | --- |
| 2.1 | A note on pre construction stage Geotechnical investigation of Daudhan dam site, by GSI, Bhopal | 1 - 12 |
| 2.2 | Geophysical investigations along the Daudhan dam axis by CSMRS, New Delhi | 1 - 57 |
| 2.3 | Site specific design Earthquake parameters for Daudhan Multipurpose Project site by IIT, Roorkee. | 1 - 34 |
| 2.4 | Report of Laboratory investigation of Rock from Daudhan dam site by CSMRS, New Delhi. | 1 - 55 |
| 2.5 | A Geotechnical note on sub-surface exploration of central spillway of Daudhan dam by GSI, Bhopal. | 1 - 8 |
| 2.6 | A Geotechnical note on sub surface Exploration of CD structures across the Main canal by GSI, Bhopal. | 1 - 81 |
| 2.7 | A Geotechnical note on sub-surface exploration of the major structures (Daudhan component dam, PH–I, Tail race channel, PH–II, Upper & lower level tunnel) | 1 - 64 |
| 2.8 | A note on pre construction stage Geotechnical investigation of the proposed Power House–II area of the exit end of lower level tunnel. | 1 - 4 |
| 2.9 | Report on Laboratory investigation of Rock from Power House, Tunnels, CD/CM structures along link canal of Daudhan dam complex by CSMRS, New Delhi. | 1 - 81 |
| 2.10 | Bearing capacity of massive sandstone of litho unit ‘A’ | 1 - 2 |
| 2.11 | Orientation and frequency of joints in massive sand stone of litho unit “A” forming foundation media for major structures | 1 - 2 |
| 2.12 | Report on Soil investigations for samples collected from Borrow areas of Daudhan dam by CSMRS, New Delhi | 1 - 94 |
| 2.13 | Report on Soil investigations for samples collected from borrow areas along link canal by CSMRS, New Delhi | 1 - 81 |
| Appendix Volume-II: Survey & Investigations |
| Appendix no. | Particulars | Page nos. |
| 2.14 | Report on the construction material survey and laboratory investigation of rock and sand samples for use as coarse aggregate and fine aggregate respectively in concrete during construction of the proposed Daudhan dam, by CSMRS, New Delhi. | 1 - 70 |
| 2.15 | Report on Petrographic analysis of Ken river silt by IIT, New Delhi | 1 - 13 |
| 2.16 | Satellite data based inputs for Feasibility Assessment of proposed irrigation projects in Upper Betwa sub basin by NRSA, Hyderabad | 1 - 136 |
| 2.17 | Note on Geotechnical investigation of Raisen & Vidisha districts of M.P. State, by GSI, Bhopal | 1 - 7 |
| 2.18 | Note on Geotechnical investigation of Makodia dam site by GSI,Bhopal | 1 - 4 |
| 2.19 | Site specific design Earthquake parameters for Makodia dam site by IIT, Roorkee. | 1 - 37 |
| 2.20 | A Geotechnical note on Sub – Surface exploration of Makodia dam site by GSI, Bhopal | 1 - 15 |
| 2.21 | Report of Laboratory testing of Rock samples from Makodia dam by IIT, New Delhi. | 1 - 23 |
| 2.22 | A Geotechnical note on sub-Surface exploration of Barari & Kesari barrage & CD structures across the main RBC & LBC of Makodia dam & RBC of Kesari barrage in Upper Betwa projects by GSI, Bhopal. | 1 - 67 |
| 2.23 | Report on Laboratory test results of Rock samples from proposed CD structures of Makodia Right Bank Canal, by IIT, New Delhi. | 1 - 6 |
| 2.24 | Report on Laboratory test results on Rock cores from CD structures of Kesari barrage right bank canal and Makodia right bank canal | 1-9 |
| 2.25 | Report on Laboratory test results on Rock samples of Barari, Kesari Barrages & Makodia Left Bank Canal locations by IIT, New Delhi. | 1 - 6 |
| 2.26 | Report on Soil investigation of Borrow area soil samples from Makodia dam by CSMRS, New Delhi. | 1 - 47 |
| 2.27 | Test results of soil samples collected from Makodia Right & Left Canal, Kesari Right Bank Canal, Barari Canal by CSMRS, New Delhi. | 1 - 33 |
| 2.28 | Report on the construction material survey and laboratory investigation of rock and sand samples for use as coarse aggregate and fine aggregate respectively in concrete during construction of the proposed Ken-Betwa link project (Upper Betwa Project) by CSMRS, New Delhi. | 1 - 32 |

APPENDIX   Volume-III: Hydrology

| Chapter No. | Particulars | Page No. |
| --- | --- | --- |
| Hydrological Studies Phase-I |
|  | Acknowledgement | i |
|  | Scientists & staff involved | ii |
|  | Executive Summary | iii – x |
| Chapter-1 | Introduction | 1 |
|  | 1.0 Introduction 1.1 Scope of work 1.2 Objectives | 1 2 2 |
| Chapter-2 | System description | 3 |
|  | 2.0 Ken And Betwa river system 2.1 Ken River Basin | 3 3 |
|  | 2.1.1 2.1.2 2.1.3 2.1.4 2.1.5 2.1.6 2.1.7 2.1.8 | Topography Geology Hydrogeology The climate Rainfall Drainage basin characteristics (up to Daudhan Dam) Major projects Previous studies | 6 6 6 7 7 7 10 13 |
|  | Betwa river basin The proposed Ken-Betwa Link project | 16 16 |
|  | 2.3.1 2.3.2 2.3.3 2.3.4 | Revised configuration of the project Command area Population affected and benefited Natural resources | 18 24 24 26 |
| Chapter- 3 | Processing of rainfall and runoff data | 27 |
|  | 3.1 Processing of rainfall data | 27 |
|  | 3.1.1 3.1.2 3.1.3 | Tests for consistency of rainfall series Arithmetic Mean (AM) method Thiessen Polygon (TP) method | 30 38 39 |
|  | 3.2 Processing of runoff data | 42 |
|  | 3.2.1 3.2.2 3.2.3 3.2.4 3.2.5 3.2.6 | Comparison plots using residual series Double mass curves Comparison of rainfall and runoff Rainfall-runoff modeling t-test F-test | 43 47 50 52 55 57 |
|  | 3.3 Conclusions 3.4 References | 58 59 |
| Chapter-4 | Water need assessment | 60 |
|  | 4.1 Water needs | 60 |
|  | 4.1.1 4.1.2 4.1.3 4.1.4 4.1.5 | Domestic water needs Irrigation needs Industrial water needs Water requirement for hydropower generation Water requirement for environmental and ecological purposes | 60 62 67 67 67 |
|  | 4.2 Regeneration 4.3 Import and Export | 67 68 |
| Chapter-5 | Water balance and yield assessment | 69 |
|  | 5.1 Water balance | 69 |
|  | 5.1.1 5.1.2 5.1.3 | Hydrological water balance equation Ground water balance equation Water use balance equation | 69 70 70 |
|  | 5.2 Yield assessment | 71 |
|  | 5.2.1 5.2.2 5.2.3 5.2.4 | Estimation of observed yield Estimation of virgin yield and upstream utilization Flow duration curve and water availability analysis Water availability analysis at Daudhan dam | 71 72 76 83 |
|  | Ground water potential Water availability and surplus 5.5 Summary | 94 96 97 |
| Chapter- 6 | Design and diversion flood | 98 |
|  | 6.0 Introduction 6.1 Design flood estimation | 98 99 |
|  | 6.1.1 6.1.2 6.1.3 6.1.4 6.1.5 | Unit hydrograph approach Segregation of daily rainfall data Loss rate and base flow UH derivation Synthetic unit hydrograph derivation for sub-catchment 2 | 99 102 103 109 113 |
|  | 6.2 Probable Maximum Precipitation (PMP) | 116 |
|  | 6.2.1 6.2.2 6.2.3 6.2.4 | Design storm Duration of design storm Critical sequencing of the PMP PMP for Gaisabad | 116 118 119 124 |
|  | 6.3 Flood hydrographs using the PMP | 129 |
|  | 6.3.1 | Routing of UH | 129 |
|  | Probable Maximum Flood for Daudhan Annual Maximum Series Model Design floods for diversion structure Summary References | 134 135 140 141 142 |
| Chapter -7 | Sedimentation of Daudhan reservoir | 144 |
|  | 7.1 Dead storage capacity of Daudhan reservoir 7.2 Total sediment volume trapped 7.3 Sediment distribution | 144 145 146 |
| Chapter -8 | Simulation Studies for Daudhan reservoir | 151 |
|  | 8.1 Reservoir capacity computation 8.2 Live storage capacity of Daudhan reservoir | 151 152 |
|  | 8.2.1 8.2.2 | Simulation under potential water use scenario Simulation under different water use scenario | 156 156 |
|  | Determining maximum water level- reservoir routing | 157 |
|  | 8.3.1 8.3.2 | Modified Puls method Reservoir routing for Daudhan | 158 159 |
|  | 8.4 Evaporation from Daudhan reservoir | 160 |
| APPENDICES |  |  |
| 3.1 | Monthly rainfall of Ken basin upto Daudhan | A-1 |
| 3.2 | Monthly Rainfall of Ken basin upto Banda | A-5 |
| 3.4 | Monthly Rainfall of Ken basin upto Garakota | A-11 |
| Chapter No. | Particulars | Page no. |
| 3.5 | Monthly Rainfall of Ken basin upto Gasiabad | A-14 |
| 4.1 | List of existing projects in Ken basin upto proposed Daudhan dam | A-17 |
| 4.2 | List of ongoing projects in Ken basin upto proposed Daudhan Dam | A-22 |
| 4.3 | List of proposed projects in Ken basin upto proposed Daudhan dam | A-23 |
| 4.4 | Irrigation water requirement | A-33 |
| 5.1 | Estimation of runoff factor for Banda gauging site | A-34 |
| 5.2 | Estimation of runoff factor for Madla gauging site | A-35 |
| 5.3 | List of existing projects in Ken basin between proposed Daudhan Dam and Banda Gauging Site | A-36 |
| 5.4 | Utilization data of Bariyarpur Pick Up Weir | A-39 |
| 5.5a | Annual utilization data of various projects upto Banda (1960-1973) | A-40 |
| 5.5b | Annual utilization data of various projects upto Banda (1974-1987) | A-45 |
| 5.5c | Annual utilization data of various projects upto Banda (1988-1999) | A-50 |
| 5.6 | Monthly upstream utilization at Banda | A-55 |
| 5.7 | Monthly upstream utilization at Madla | A-57 |
| 6.1 | Design Strom Study For Four Projects on Ken- Betwa Link Project | A-58 |

| Chapter No. | Particulars | Page No. |
| --- | --- | --- |
|  | Hydrological Studies Phase-II (A) |  |
|  | Acknowledgement | Xi |
|  | Scientists & staff involved | xii |
|  | Executive Summary | xiii – xviii |
| Chapter-1 | Introduction | 163 |
|  | 1.0 Introduction 1.1 Scope of Work 1.2 Objectives | 163 164 164 |
| Chapter-2 | System Description | 166 |
|  | Betwa river system | 166 |
|  | 2.0.1 2.0.2 2.0.3 2.0.4 2.0.5 2.0.6 | Topography Geology Climate Rainfall Drainage basin characteristics Major projects and previous studies | 172 172 172 172 173 175 |
| Chapter-3 | Processing of Rainfall and Runoff Data | 185 |
|  | 3.1 Processing of rainfall data | 185 |
|  | 3.1.1 3.1.2 3.1.2.1 3.1.2.2 3.1.3 3.1.3.1 3.1.3.2 | Tests for consistency of rainfall series Estimation of areal average rainfall Arithmetic Mean (AM) method Thiessen Polygon (TP) method Tests for consistency of average annual rainfall t-test F-test | 185 196 197 197 201 201 202 |
|  | 3.2 Processing of Runoff Data | 203 |
|  | 3.2.1 3.2.2 3.2.3 3.2.4 3.2.5 | Estimation of observed yield Test of consistency for yield Comparison of rainfall and runoff Rainfall-runoff Modeling t and F tests | 203 204 205 206 206 |
|  | 3.3 Conclusions 3.4 References | 207 207 |
| Chapter-4 | Water Need Assessment | 208 |
|  | 4.1 Water needs | 208 |
|  | 4.1.1 4.1.2 4.1.3 | Domestic water needs Irrigation needs Industrial water needs | 208 210 216 |
|  | 4.1.4 4.1.5 | Water requirement for hydropower generation Water requirement for environmental and ecological purposes | 216 216 |
|  | 4.2 Regeneration 4.3 Import and export 4.4 Summary | 216 217 217 |
| Chapter-5 | Water balance and yield assessment | 218 |
|  | 5.1 Water Balance | 218 |
|  | 5.1.1 5.1.2 5.1.3 | Hydrological water balance equation Ground water balance equation Water use balance equation | 218 219 219 |
|  | 5.2 Yield Assessment | 220 |
|  | 5.2.1 5.2.2 5.2.3 5.2.4 | Estimation of observed yield Estimation of virgin yield and upstream utilization Flow duration curve and water availability analysis Water availability analysis at Projects sites | 220 220 223 227 |
|  | 5.3 Water utilization by proposed projects 5.4 Ground water potential 5.5 Water Availability and Surplus 5.6 Summary | 241 244 246 249 |
| Chapter- 6 | Design and Diversion Flood | 250 |
|  | 6.0 Introduction 6.1 Design Flood Estimation | 250 250 |
|  | 6.1.1 6.1.2 6.1.3 6.1.4 6.1.5 6.1.6 6.1.7 | Unit hydrograph approach Gauge and discharge relationship Segregation of daily rainfall data Unit hydrograph derivation for Basoda by Nash method Synthetic unit hydrograph derivation for Basoda sub-catchment Validation of flood hydrograph Synthetic unit hydrograph derivation for sub-catchments | 251 252 257 265 268 270 271 |
|  | 6.2 Probable Maximum Precipitation (PMP) | 276 |
|  | 6.2.1 6.2.2 6.2.3 | Design storm Duration of design storm Critical sequencing of the PMP | 276 277 278 |
|  | 6.3 Flood hydrographs using the PMP & SPS 6.4 Annual Maximum Series Model | 285 288 |
|  | 6.4.1 6.4.2 6.4.3 | Test for independence and stationarity Homogeneity and stationarity tests Test for outliers | 288 289 290 |
|  | 6.5 Design Floods for Diversion Structure 6.6 Summary 6.7 References | 293 294 295 |
| Chapter-7 | Sedimentation of Makodia Reservoir | 296 |
|  | 7.1 Dead Storage Capacity of Makodia Reservoir 7.2 Total Sediment Volume Trapped 7.3 Sediment Distribution | 296 297 297 |
| Chapter-8 | Simulation Studies for Makodia Reservoir | 303 |
|  | 8.1 Reservoir Capacity Computation 8.2 Live Storage Capacity of Makodia Reservoir | 303 304 |
|  | 8.2.1 8.2.2 8.2.3 8.2.4 8.2.5 8.2.6 8.2.7 | Simulation of operation of Makodia Reservoir with FRL at 437.15 m Sizing of Makodia Reservoir if Barari Barrage is Dropped Additional Command Area That Can Be Served by Makodia Reservoir Finalization of FRL of Makodia Reservoir Simulation of operation of Barari Barrage Simulation of operation of Kesari Barrage Evaporation from Various Reservoirs | 306 306 306 307 307 308 309 |
|  | Determining Maximum Water Level-Reservoir Routing for Makodia | 309 |
| Chapter-9 | Design of Canal from Barwa Sagar to Parichha Weir by Lacey’s theory | 311 |

| No. | Particulars | Page No. |
| --- | --- | --- |
| 3.1 3.2 3.3 3.4 3.5 | Appendices Recorded and corrected annual rainfall at three stations Monthly Rainfall (mm) of Upper Betwa basin up to Basoda Monthly Rainfall (in MM) of Upper Betwa basin up to Barari Monthly Rainfall (in MM) of Upper Betwa basin up to Makodia Monthly Rainfall (in MM) of Upper Betwa basin up to Kesari | A-81 A-82 A-85 A-88 A-91 |
| 4.1 4.2 4.3 4.4 4.5 4.6 4.7 4.8 4.9 | List of existing projects in Betwa basin up to Makodia project site List of ongoing projects in Betwa basin up to Makodia project site List of proposed projects in Betwa basin up to Makodia project site List of existing projects in Betwa basin up to Barari project site List of ongoing projects in Betwa basin up to Barari project site List of proposed projects in Betwa basin up to Barari project site List of existing projects in Betwa basin up to Kesari project site List of ongoing projects in Betwa basin up to Kesari project site List of proposed projects in Betwa basin up to Kesari project site | A-94 A-94 A-94 A-95 A-96 A-96 A-97 A-98 A-98 |
| 5.1 5.2 5.3 | List of existing projects up to Basoda G&D site Monthly utilization at Kaliasot and Kerwan Upstream utilization (MCM) at Basoda excluding the BadaTalab catchment and Halali | A-99 A-101 A-102 |

|  | Hydrological Studies Phase-II (B) |  |
| --- | --- | --- |
|  | Acknowledgement | xix |
|  | Scientists & staff involved IN Phase-II B & C | xx |
|  | Executive Summary | xxi – xxii |
| Chapter-1 | Introduction | 314 |
| Chapter-2 | Brief Description of NWS-DAMBRK MODEL | 315 |
| 2.1 | Assumptions | 315 |
| 2.2 | Data Requirement | 315 |
| 2.3 | Program Capabilities | 316 |
| 2.4 | Other Capabilities | 317 |
| Chapter-3 : Methodology | 318 |
| 3.1 | Reservoir Routing | 318 |
| 3.2 | Reservoir Outflow Computation | 319 |
| Chapter-4: Study Area | 321 |
| 4.1 | Ken River Basin | 321 |
| 4.2 | Topography | 321 |
| 4.3 | Geology | 323 |
| Chapter-5: | Dam Break Analysis | 324 |
| 5.1 | Comparative Analysis of cases 1-3 | 333 |
| 5.2 | Summary results of computed maximum water levels in Ken river | 333 |
| Chapter-6: Sensitivity Analysis | 335 |
| Chapter-7: Summary and conclusions | 341 |
| Appendices |  |  |
| Appendix-I | Input data for Case 1 | A-103 |
| Appendix-II | Input data for Case 2 | A-108 |
| Appendix-III | Input data for Case 3 | A-113 |
| Appendix-IV A | Cross sections at different elevations u/s of Daudhan Reservoir | A-118 |
| Appendix-IV B | Cross sections at different elevations d/s of Daudhan reservoir | A-123 |

| Chapter No. | Particulars | Page No. |
| --- | --- | --- |
|  | Hydrological Studies Phase-II I |  |
| Chapter- 1 | Backwater profile for Daudhan and Makodia dam | 343 |
| 1.1 | Backwater Profile for Daudhan dam | 343 |
| 1.2 | Backwater Profile for Makodia dam | 343 |
| Chapter- 2 | Morphology Analysis for Ken River from Daudhan dam to Banda | 345 |
| 2.1 | Morphology analysis for Ken river from Daudhan dam to Banda | 345 |
| 2.2 | Ken river morphology | 345 |
| Chapter-3 | Computation of Maximum Water Level from Daudhan to Madla | 348 |
| Chapter-4 | Impact of Daudhan Dam on Downstream Flood Conditions | 350 |
| 4.1 | Impact of Daudhan dam on downstream flood conditions | 350 |
| Chapter- 5 | Multi Reservoir Simulation of Ken-Betwa System | 352 |
| 5.1 | Makodia dam | 354 |
| 5.2 | Barari barrage | 355 |
| 5.3 | Kesari barrage | 357 |
| 5.4 | Rajghat dam | 358 |
| 5.5 | Matatila dam | 359 |
| 5.6 | Dhukwan dam | 360 |
| 5.7 | Daudhan dam | 361 |
| 5.8 | Ken-Betwa link | 362 |
| 5.9 | Parichha weir | 364 |
| 5.10 | Inflow to the reservoirs/barrages | 364 |
| 5.11 | Results of simulation of scenarios | 365 |

Appendix Volume – IV: Cost Estimate

| Annexure no. | Particulars | Page no. |
| --- | --- | --- |
| 10.0 | General Abstract of Cost | 1 |
| 10.1 | General Abstract of Unit-I Head Works (Daudhan Dam) | 5 |
| 10.1.1 | A - Preliminary | 6 |
|  | A1 – Topographical surveys | 7 |
|  | A2 - Hydrological & Meteorological surveys | 8 |
|  | A3 – Geological & Geotechnical surveys | 9 |
|  | A4 – Investigations for availability of Construction Materials | 10 |
|  | A5 – Seismic Studies | 11 |
|  | A6 – Construction of access Roads to facilitate site investigations | 12 |
|  | A7 – Charges for consultation for preparation of DPR | 13 |
|  | A8 – Preparation of Project Report | 14 |
| 10.1.2 | B - Land | 15 |
| 10.1.3 | C - Works | 19 |
|  | C1 – Earth dam | 20 |
|  | C2 – Non over flow section | 26 |
|  | C3 – Over flow section | 30 |
| 10.1.4 | K - Buildings | 35 |
|  | K1 – Non Residential buildings | 36 |
|  | K2 – Residential buildings | 37 |
| 10.1.5 | L - Earthwork | 40 |
| 10.1.6 | M - Plantation | 43 |
| 10.1.7 | O - Miscellaneous | 44 |
|  | O1- Analysis of rates for electrification | 47 |
| 10.1.8 | P - Maintenance | 48 |
| 10.1.9 | Q - Special T&P | 49 |
| 10.1.10 | R - Communications | 52 |
| 10.1.11 | X - Environment & Ecology | 54 |
| 10.2 | General Abstract of Cost Unit-I Head Works –Upper Betwa Projects | 59 |
| 10.2.1 | A - Preliminary | 60 |
| 10.2.2 | B - Land | 61 |
| 10.2.3 | C - Works | 65 |
|  | C1 – Makodia dam | 66 |
|  | C1.1- Earth dam | 67 |
|  | C1.2 – Non over flow section | 72 |
|  | C1.3 – Over flow section | 75 |
|  | C2 - Barari barrage | 80 |
|  | C3 - Kesari barrage | 82 |
| 10.2.4 | K - Buildings | 83 |
| Annexure no. | Particulars | Page no. |
|  | K1 - Non residential buildings | 84 |
|  | K2 - Residential buildings | 85 |
| 10.2.5 | M - Plantation | 88 |
| 10.2.6 | O - Miscellaneous | 89 |
|  | O1 – Analysis of rates for electrification | 93 |
| 10.2.7 | P - Maintenance | 94 |
| 10.2.8 | Q - Special T&P | 95 |
| 10.2.9 | R - Communications | 97 |
| 10.2.10 | X - Environment & Ecology | 99 |
| 10.3 | General Abstract of Cost Unit-II: Canal System (Ken-Betwa Link Canal) | 103 |
| 10.3.1 | A - Preliminary | 104 |
|  | A1 – Topographical surveys | 105 |
|  | A2 – Geological & Geotechnical Surveys | 106 |
|  | A3 – Investigation for availability of Construction Materials | 107 |
|  | A4 – Vehicles for Inspection Officers for site investigations | 108 |
|  | A5 – Surveys & Camp Equipments | 109 |
|  | A6 – Charges for consultation for preparation of DPR | 110 |
|  | A7 – Actual expenditure on Establishment | 111 |
| 10.3.2 | B-Land | 112 |
| 10.3.3 | C - Works | 113 |
|  | C1 – Tunnel intake structure for Upper level tunnel – 57.70 km length | 114 |
|  | C2 – Upper level tunnel- 1871.15m length | 118 |
| 10.3.4 | D-Regulators | 120 |
| 10.3.5 | E-Falls | 122 |
| 10.3.6 | F-Cross drainage structures | 123 |
|  | F1 – Syphon aqueduct | 124 |
|  | F2 – Aqueduct | 125 |
|  | F3 – Canal syphon | 126 |
|  | F3.1 – Canal Siphon at Dhasan river crossing | 127 |
| 10.3.7 | G – Bridges | 129 |
| 10.3.8 | H – Escapes | 130 |
| 10.3.9 | K – Buildings | 131 |
|  | K1 – Non-residential buildings | 132 |
|  | K2 – Residential buildings | 133 |
| 10.3.10 | L-Earthwork & Lining | 136 |
|  | L1 – Main canal | 137 |
|  | L2 – Branch canals | 141 |
| Annexure no. | Particulars | Page no. |
|  | L1.1 –Detailed estimate of earthwork of Ken-Betwa link canal (218.695 km) | 142 |
| 10.3.11 | M-Plantation | 236 |
| 10.3.12 | O-Miscellaneous | 237 |
| 10.3.13 | P-Maintenance | 239 |
| 10.3.14 | Q-Special T&P | 240 |
| 10.3.15 | R-Communications | 242 |
| 10.3.16 | U-Distributaries/Minors | 243 |
| 10.3.17 | V-Field channels & Water courses | 244 |
| 10.3.18 | W-Drainage | 245 |
| 10.3.19 | X-Environment & Ecology | 246 |
| 10.4 | General Abstract of Cost Unit-II Canal System(KEN LBC system) | 248 |
| 10.4.1 | Abstract cost of A-Preliminary | 249 |
|  | A1 – Ken LBC | 250 |
|  | A2 – Mukhna & Kurraha lift | 253 |
|  | A3 – Lugasi & Satna lift | 256 |
|  | A4 – Urmil RBC contour and ridge | 259 |
| 10.4.2 | Abstract cost of B- Land | 262 |
|  | B1 – Ken LBC & 2.2 km connecting canal from PH-II to Ken LBC | 264 |
|  | B2 – Mukna lift | 265 |
|  | B3 – Kurraha lift | 266 |
|  | B4 – Lugasi lift | 267 |
|  | B5 – Satna lift | 268 |
|  | B6 – Urmil RBC (Contour canal) | 269 |
|  | B7 – Urmil RBC(ridge canal) | 270 |
| 10.4.3 | C-Works Abstract cost of Lower Level Tunnel | 271 |
|  | C1 – Cost of Intake structure for Lower Level Tunnel | 272 |
|  | C2 – Cost of Lower Level Tunnel- 1068.21 m length | 277 |
|  | C3 – Cost of Surge Tank for Lower Level Tunnel | 279 |
| 10.4.4 | Abstract cost of D-Regulators | 282 |
|  | D1 – Ken LBC | 283 |
|  | D1 – Mukhna lift | 283 |
|  | D1 – Satna lift | 284 |
|  | D1 – Kurraha lift | 284 |
|  | D1 – Lugasi lift | 285 |
|  | D1 – Urmil RBC (Contour canal) | 286 |
|  | D1 – Urmil RBC (Ridge canal) | 287 |
| 10.4.5 | Abstract cost of E – Falls | 288 |
|  | E1 – Ken LBC & Urmil RBC ridge canal | 289 |
| Annexure no. | Particulars | Page no. |
| 10.4.6 | Abstract cost of F-Cross drainage works | 290 |
|  | F1 – Ken LBC | 291 |
|  | F2 – Mukhna lift | 293 |
|  | F3 – Kurraha lift | 295 |
|  | F4 – Lugasi lift | 297 |
|  | F5 – Satna lift | 299 |
|  | F6 – Urmil RBC contour canal | 301 |
|  | F7 – Urmil RBC ridge canal | 303 |
| 10.4.7 | Abstract of Cost of G – Bridges | 305 |
|  | G1 – Ken LBC | 306 |
|  | G1 – Mukhna lift | 306 |
|  | G1 – Satna lift | 306 |
|  | G2 – Kurraha lift | 307 |
|  | G2 – Lugasi lift | 307 |
|  | G3 – Urmil RBC Contour canal | 308 |
|  | G3 – Urmil RBC Ridge canal | 308 |
| 10.4.8 | General Abstract cost of H- Escapes | 309 |
|  | H1 – Ken Left Bank Canal | 310 |
|  | H1 – Kurraha lift | 310 |
|  | H1 – Lugasi lift | 310 |
|  | H1- Urmil RBC contour canal | 310 |
| 10.4.9 | Abstract of cost of S & J sub-head for lift canals including a note on the estimate of S (Power plant and Electrical system) and J (Civil works) of lift canals | 311 |
| 10.4.10 | Abstract of cost of K-Buildings | 316 |
|  | K1 – Non-residential buildings | 317 |
|  | K2 – Residential buildings | 318 |
| 10.4.11 | Abstract of cost of L- Earthwork & Lining | 321 |
|  | L1 – Ken LBC | 322 |
|  | L2 – Mukhna lift | 324 |
|  | L3 – Kurraha lift | 326 |
|  | L4 – Lugasi lift | 328 |
|  | L5 – Satna lift | 330 |
|  | L6 – Urmil RBC contour canal | 332 |
|  | L7 – Urmil RBC ridge canal | 334 |
|  | L8 – Abstract of cost of Canals lining | 336 |
| 10.4.12 | Abstract of cost of M – Plantation | 337 |
| 10.4.13 | Abstract of cost of O – Miscellaneous | 338 |
| 10.4.14 | Abstract of cost of P – Maintenance | 342 |
| 10.4.15 | Abstract of cost of Q – Special T & P | 343 |
| 10.4.16 | Abstract of cost of R – Communications | 345 |
| Annexure no. | Particulars | Page no. |
| 10.4.17 | Abstract of cost of U – Distributory and Minors | 346 |
|  | U1 – Ken LBC | 347 |
|  | U2 – Mukhna lift | 348 |
|  | U3 – Kurraha lift | 349 |
|  | U4 – Lugasi lift | 350 |
|  | U5 – Satna lift | 351 |
|  | U6 – Urmil RBC contour canal | 352 |
|  | U7 – Urmil RBC ridge canal | 353 |
| 10.4.18 | Abstract of cost of V- Water courses & field channels | 354 |
| 10.4.19 | Abstract of cost of W-Drainage | 355 |
| 10.4.20 | X- Environment & Ecology | 356 |
| 10.5 | General Abstract of cost of Unit-II:Upper Betwa Canal system | 358 |
| 10.5.1 | A – Preliminary | 359 |
| 10.5.2 | B – Land | 360 |
| 10.5.3 | C- Works | 361 |
| 10.5.4 | D – Regulators | 362 |
| 10.5.5 | E – Falls | 363 |
| 10.5.6 | F – Cross drainage structures | 364 |
|  | F1 – Syphon Aqueducts | 365 |
|  | F2 – Super Passages | 366 |
|  | F3 – Pipe culverts | 367 |
|  | F4 – Canal syphons | 368 |
| 10.5.7 | G – Bridges | 369 |
| 10.5.8 | H – Escapes | 370 |
| 10.5.9 | K – Buildings | 371 |
|  | K1 – Non-residential buildings | 372 |
|  | K2 – Residential buildings | 373 |
| 10.5.10 | L – Earthwork & Lining | 376 |
|  | L1 – Cost of Makodia RBC & LBC,Barari ridge canal and Kesari RBC | 377 |
|  | L2 – Cost of branch canals under Makodia RBC & LBC, Barari ridge canal and Kesari RBC | 381 |
| 10.5.11 | M – Plantation | 382 |
| 10.5.12 | O – Miscellaneous | 383 |
| 10.5.13 | P - Maintenance | 385 |
| 10.5.14 | Q – Special T& P | 386 |
| 10.5.15 | R – Communications | 388 |
| 10.5.16 | U – Distributaries & Minors | 389 |
| 10.5.17 | V – Water courses & Field Channels | 390 |
| 10.5.18 | W – Drainage | 391 |
| Annexure no. | Particulars | Page no. |
| 10.5.19 | X - Environment & Ecology | 392 |
| 10.6 | General Abstract of cost of Unit-III: Power(Power House-I) | 394 |
| 10.6.1 | A – Preliminary | 395 |
| 10.6.2 | B – Land | 396 |
| 10.6.3 | J – Power Plant Civil works | 397 |
|  | J1 – Penstock | 398 |
|  | J2 – Power house complex | 400 |
|  | J3 – Tail Race Channel | 401 |
| 10.6.4 | M- Plantation | 402 |
| 10.6.5 | O – Miscellaneous | 403 |
| 10.6.6 | P – Maintenance | 404 |
| 10.6.7 | R-Communications | 405 |
| 10.6.8 | S – Electro-mechanical works | 406 |
|  | S1 – Preliminary | 407 |
|  | S2 – Generator, Turbine and Accessories | 408 |
|  | S3 – Auxiliary Electrical Equipment for power station | 409 |
|  | S4 – Auxiliary Mechanical Equipment and services for power station | 410 |
|  | S5 – Sub-station equipments and auxiliary equipments & service for the switch yard | 411 |
| 10.7 | General Abstract of Unit-III: Power (Power House-II) | 412 |
| 10.7.1 | A – Preliminary | 413 |
| 10.7.2 | B – Land | 414 |
| 10.7.3 | J – Power Plant Civil Works | 415 |
|  | J1 – Penstock | 416 |
|  | J2 – Power house complex | 418 |
|  | J3 – Tail Race Channel | 419 |
| 10.7.4 | M – Plantation | 420 |
| 10.7.5 | O – Miscellaneous | 421 |
| 10.7.6 | P – Maintenance | 422 |
| 10.7.7 | Q – Special T & P | 423 |
| 10.7.8 | R – Communications | 425 |
| 10.7.9 | S – Electromechanical works | 426 |
|  | S1 – Preliminary | 427 |
|  | S2 – Generator, Turbine and Accessories | 428 |
|  | S3 – Auxiliary Electrical Equipment for power station | 429 |
|  | S4 – Auxiliary Mechanical Equipment and services for power station | 430 |
|  | S5 – Sub-station Equipments and auxiliary equipments & service for the switch yard | 431 |
| 10.8 | Abstract of cost of Unit-VI: Command Area Development W – Drainage | 432 |

Drawing Volume:I –Main component(S&I)

| Sl. No. | Title | Plate No. |
| --- | --- | --- |
| 1 | Index Map of Ken-Betwa Link Project | 1.1 |
| 2 | Longitudinal section of Ken river between Daudhan & Gangau weir | 2.1.1 |
| 3 | Cross-section of Ken river between Daudhan dam site & Banda G&D site | 2.1.2 (18 Nos.) |
| 4 | Submergence area map of Daudhan reservoir | 2.1.3 |
| 5 | A detailed contour plan of Daudhan dam project area showing tentative location of spillway, Power house-I & II and proposed tunnels | 2.1.4 |
| 6 | Contour plan of Daudhan dam axis | 2.1.5 |
| 7 | Plant & Colony layout for Daudhan dam | 2.1.6 |
| 8 | Contour plan, Condensed L-section of link canal from RD 0.00 to 218.023 km | 2.1.7 (88 Nos.) |
| 9 | L.S & C.S. of Barwa nalla from Barwasagar reservoir to confluence with Betwa river | 2.1.8 (2 Nos.) |
| 10 | Grid surveys, L.S. and C.S. of various CD/CM structures along the link canal | 2.1.9 (25 Nos.) |
| 11 | Contour plan of Power House-I | 2.1.10 |
| 12 | Contour plan of Power House-II | 2.1.11 |
| 13 | Contour plan & L.S. of connecting canal from Power house –II to Ken Left bank canal | 2.1.12 |
| 14 | L-section of Upper Level Tunnel | 2.1.13 |
| 15 | L-section of Lower Level Tunnel | 2.1.14 |
| 16 | Map showing the enroute command area of Ken-Betwa link canal | 2.1.15 (1/4) |
| 17 | Map showing the sample command area of K-B link near Bamhori Kala village | 2.1.15 (2/4) |
| 18 | Command area map of existing Ken command in U.P. through Bariyarpur PUW | 2.1.15 (3/4) |
| 19 | Command area map of Ken LBC (M.P.) | 2.1.15 (4/4) |
| 20 | Submergence area map of Barwa Sagar reservoir | 2.1.16 |
| 21 | Map showing Communication network of the project area of Daudhan complex | 2.1.17 |
| 22 | Location of borrow areas in the vicinity of Daudhan dam | 2.1.18 |

Drawing Volume:II –

Upper Betwa component(S&I)

| Sl. No. | Title | Plate No. |
| --- | --- | --- |
| 23 | Index Map of Ken-Betwa Link Project | 1.1 |
| 24 | Longitudinal section of Betwa river U/s and D/s of Makodia dam | 2.2.1 (11 Nos.) |
| 25 | Cross-section of Betwa river U/s and D/s of Makodia dam | 2.2.2(65 Nos.) |
| 26 | Contour Plan of Submergence area map of Makodia reservoir | 2.2.3 |
| 27 | Contour plan & L-section of Makodia dam | 2.2.4 |
| 28 | Drawing showing Colony area of Makodia dam | 2.2.5.1 |
| 29 | Drawing showing plant area of Makodia dam | 2.2.5.2 |
| 30 | Contour plan, Condensed L-section of Right Bank canal of Makodia dam from RD 0.00 to 83.38 km | 2.2.6(56 Nos.) |
| 31 | Contour plan, Condensed L-section of Left Bank canal of Makodia dam from RD 0.00 to 6.74 km | 2.2.7 (5 Nos.) |
| 32 | Grid surveys, L.S. and C.S. of various canal structures across Right Bank canal of Makodia dam | 2.2.8 (15 Nos.) |
| 33 | Grid surveys, L.S. and C.S. of various canal structures across Left Bank canal of Makodia dam | 2.2.9 |
| 34 | Map showing the enroute command of Makodia canal system | 2.2.10 |
| 35 | Map showing the enroute command of Upper Betwa Project | 2.2.11 |
| 36 | Communication network of the project area of Upper Betwa projects | 2.2.12 |
| 37 | Location of borrow areas in the vicinity of Makodia dam | 2.2.13 |
| 38 | Drawing showing L-section of Betwa river (3km u/s and 3 km d/s ) | 2.3.1 |
| 39 | Cross-section of Betwa river U/s and D/s of Barari barrage | 2.3.2 |
| 40 | Pondage area map of Barari barrage | 2.3.3 |
| 41 | Contour plan of the headwork area of Barari barrage | 2.3.4 |
| 42 | Contour plan, Condensed L-section of Barari ridge canal from RD 0.00 to 4.5 km | 2.3.5 (3 Nos.) |
| 43 | OFD map of Barari command | 2.3.6 |
| 44 | Longitudinal section of Keoton river (3 km U/s and D/s) | 2.4.1 |
| 45 | Cross-section of Keotan river U/s and D/s of Kesari barrage | 2.4.2 |
| 46 | Pondage area map of Kesari barrage | 2.4.3 |
| Sl. No. | Title | Plate No. |
| 47 | Contour plan of the headwork area of Kesari barrage | 2.4.4 |
| 48 | Plant and Colony layout for Kesari barrage | 2.4.5 |
| 49 | Contour plan, Condensed L-section of Kesari right bank canal from RD 2.9 to 12.55 km | 2.4.6 (7 Nos.) |
| 50 | Grid survey, L.S. and C.S. of various canal structures across Right Bank Canal of Kesari Barrage | 2.4.7 (2 Nos) |

Drawing Volume:III – A (Main component – Design)

| Sl. No. | Title | CWC drawing No. | Plate No. |
| --- | --- | --- | --- |
| 51 | Index map of Ken Betwa Link Project |  | 1.1 |
| 52 | General Layout Plan of Daudhan Dam | KBL-7230-P-1002 | 4.1 |
| 53 | Evaluation of shear parameters Foundation soils | KBL-7230-P-203 | 4.2 |
| 54 | General lay out plan (Concrete dam) of Daudhan Dam | KBL-7230-P-101 | 4.3 |
| 55 | Daudhan Earth dam – calculation for free board | KBL-7230-P-201 | 4.4 |
| 56 | Daudhan Earth dam upstream coffer dam section & details | KBL-7230-P-208 | 4.5 |
| 57 | Typical- section and details of Daudhan Earth dam | KBL-7230-P-207 | 4.6 |
| 58 | Evaluation of shear parameters borrow area soils | KBL-7230-P-202 | 4.7 |
| 59 | Daudhan Earth Dam Stability analysis of upstream slope | KBL-7230-P-204 | 4.8 |
| 60 | Stability analysis of down stream slope with TWL | KBL-7230-P-205 | 4.9 |
| 61 | Stability analysis of down stream slope with out TWL | KBL-7230-P-206 | 4.10 |
| 62 | Daudhan Earth dam U/S & D/S wraparound details | KBL-7230-P-214 | 4.11 |
| 63 | Daudhan Earth dam surface drainage arrangement | KBL-7230-P-213 | 4.12 |
| 64 | Daudhan Earth dam Foundation Treatment | KBL-7230-P-209 | 4.13 |
| 65 | Daudhan Earth dam Plan & L-section | KBL-7230-P-210 | 4.14 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 66 | Daudhan Earth dam section at various RD’s (RD 925.00 m, 1100.00 & 1300.00m) | KBL-7230-P-211 | 4.15 |
| 67 | Daudhan Earth dam section at various RD’s (RD 1500.00 m, 1950.00 & 2065.00 m) | KBL-7230-P-212 | 4.16 |
| 68 | Maximum Non overflow section of Daudhan Dam | KBL-7230-P-103 | 4.17 |
| 69 | Zoning of materials (N.O.F. Section) of Daudhan Dam | KBL-7230-P-104 | 4.18 |
| 70 | Water stop details (N.O.F. Section) of Daudhan Dam | KBL-7230-P-107 | 4.19 |
| 71 | Maximum overflow section of Daudhan Dam | KBL-7230-P-102 | 4.20 |
| 72 | Zoning of materials (O.F. Section) of Daudhan Dam | KBL-7230-P-105 | 4.21 |
| 73 | Water stop details (O.F. Section) of Daudhan Dam | KBL-7230-P-106 | 4.22 |
| 74 | Radial gate (16000mm x 18500mm) of Daudhan Dam Spillway Sheet 1 of 2 | KBL-7230-P-1501 | 4.23 |
| 75 | Radial gate (16000m x 18500m) of Daudhan Dam Spillway Sheet 2 of 2 | KBL-7230-P-1502 | 4.24 |
| 76 | 16000mm x 1900mm (each unit) stoplog for Daudhan Dam Spillway radial gate | KBL-7230-P-1503 | 4.25 |
| 77 | Irrigation sluice gate (1600mm x 2400mm) of Daudhan Dam Sheet 1 of 2 | KBL-7230-P-1504 | 4.26 |
| 78 | Irrigation sluice gate (1600mm x 2400mm) of Daudhan Dam Sheet 2 of 2 | KBL-7230-P-1505 | 4.27 |
| 79 | River sluice arrangements of Daudhan Dam | KBL-7230-P-108 | 4.28 |
| 80 | Divide and Training wall of Daudhan Dam | KBL-7230-P-109 | 4.29 |
| 81 | Intake Structure-Plan & Sectional of Details Upper level tunnel Sheet 1 of 3 | KBL-7230-P-1151 | 4.30 |
| 82 | Intake Transition Details of Upper level tunnel Sheet 2 of 3 | KBL-7230-P-1152 | 4.31 |
| 83 | Trash rack metal Structure Details of Upper level tunnel Sheet 3 of 3 | KBL-7230-P-1153 | 4.32 |
| 84 | Longitudinal- section of Upper level tunnel | KBL-7230-P-1154 | 4.33 |
| 85 | Typical Excavation & Rock Support Details of Upper level tunnel (Drill And Blast Method) | KBL-7230-P-1155 | 4.34 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 86 | Typical Concrete Lining & Grouting Details of Upper level tunnel | KBL-7230-P-1156 | 4.35 |
| 87 | Exit Portal Details of Upper level tunnel | KBL-7230-P-1157 | 4.36 |
| 88 | Details of Transition after Exit Portal Upper level tunnel | KBL-7230-P-1158 | 4.37 |
| 89 | Intake Service & Emergency Gate (6000mm x 6000mm) Upper Level Tunnel General Installation Sheet 1 of 2 | KBL-7230-P-1510 | 4.38 |
| 90 | Intake Service & Emergency Gate (6000mm x 6000mm) Upper Level Tunnel General Installation Sheet 2 of 2 | KBL-7230-P-1511 | 4.39 |
| 91 | L- section of K-B Link canal | KBL-7230-D-2501 to 2554 | 4.40 to 4.93 |

Drawing Volume:III – B (Main Component –Design)

| 92 | Index map of Ken Betwa Link Project |  | 1.1 |
| --- | --- | --- | --- |
| 93 | L- section of K-B Link canal | KBL-7230-D-2555 to 2588 | 4.94 to 4.127 |
| 94 | Details of lined Section of K-B Link canal | KBL-7230-D-2589 | 4.128 |
| 95 | Cross Section of K-B Link canal | KBL-7230-D-2590 | 4.129 |
| 96 | Drainage arrangement of Lined Canal | KBL-7230-D-2591 | 4.130 |
| 97 | Mechanical Placement of Lining (K-B Link canal) | KBL-7230-D-2592 | 4.131 |
| 98 | Details of distribution Network (K-B Link canal) | KBL-7230-D-2599 | 4.132 |
| 99 | Details of Typical Cross regulator | KBL-7230-D-2600 | 4.133 |
| 100 | 3500mm x 4500mm Service gates and 1750mm x 4500mm stoplog of K-B Link Cross regulator general Installation sheet 1 of 2 | KBL-7230-P-1515 | 4.134 |
| 101 | 3500mm x 4500mm Service gates and 1750mm x 4500mm stoplog general Installation sheet 2 of 2 | KBL-7230-P-1516 | 4.135 |
| 102 | Details of settling basin at RD 250m | KBL-7230-D-2593 | 4.136 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 103 | Exit Regulator Details | KBL-7230-D-2594 | 4.137 |
| 104 | Details of Typical Major Bridge (K-B Link canal) | KBL-7230-D-2595 | 4.138 |
| 105 | Details of Typical Aqueduct (K-B Link canal) | KBL-7230-D-2596 | 4.139 |
| 106 | Details of Typical Syphon Aqueduct (K-B Link canal) | KBL-7230-D-2596-A | 4.140 |
| 107 | Details of Canal Syphon on Dhasan river | KBL-7230-D-2597 | 4.141 |
| 108 | Details of Typical Canal Fall (K-B Link canal) | KBL-7230-D-2598 | 4.142 |
| 109 | KMPP Condensed L- Section of Ken L.B.C. RD.0.0 to 600 | - | 4.143 |
| 110 | KMPP Condensed L- Section of Ken L.B.C. RD.600 to 1200 | - | 4.144 |
| 111 | KMPP Condensed L- Section of Ken L.B.C. RD.1200 to 1800 | - | 4.145 |
| 112 | KMPP Condensed L- Section of Ken L.B.C. RD.1800 to 2110 | - | 4.146 |
| 113 | Link Canal to KMPP: L- section RD 0.0 to RD 2.2 Km | KBL-7230-D-2680 | 4.147 |
| 114 | Link Canal to KMPP: Details of Cross Section of Canal | KBL-7230-D-2681 | 4.148 |
| 115 | Alternative Studies | KBL-7230-P-1001 | 4.149 |
| 116 | General Layout plan of PH-I, PH-II and Upper Level Tunnels | KBL-7230-P-1002 | 4.150 |
| 117 | Intake structure-Plan & Sectional Details Dam toe PH-I Sheet 1 of 3 | KBL-7230-P-1003 | 4.151 |
| 118 | Intake Transition Details of Dam toe PH-I Sheet 2 of 3 | KBL-7230-P-1004 | 4.152 |
| 119 | Trash rack metal Structure Details of Dam toe PH-I Sheet 3 of 3 | KBL-7230-P-1005 | 4.153 |
| 120 | 3800mm x4500mm intake Service gates & stoplogs dam toe power House –I general installation sheet 1 of 2 | KBL-7230-P-1506 | 4.154 |
| 121 | Intake Service gates & stoplogs (3800mm x4500mm ) dam toe power House –I general installation sheet 2 of 2 | KBL-7230-P-1507 | 4.155 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 122 | Penstock Steel Liner Details of Dam toe PH-I | KBL-7230-P-1006 | 4.156 |
| 123 | Penstock Steel Liner Typical Details of Dam toe PH-I | KBL-7230-P-1007 | 4.157 |
| 124 | 5000mm x 4400mm Draft Tube Gate for Power House-I (Daudhan Dam) General Installation | KBL-7230-P-1513 | 4.158 |
| 125 | Cross Section of Dam toe PH-I | KBL-7230-P-1008 | 4.159 |
| 126 | M.I.V. Floor Layout Plan at EL 218.00 M Dam toe PH-I | KBL-7230-P-1009 | 4.160 |
| 127 | Turbine Floor Layout Plan at EL 225.0 M Dam toe PH-I | KBL-7230-P-1010 | 4.161 |
| 128 | Generator Floor Layout Plan at EL 229.0 M Dam toe PH-I | KBL-7230-P-1011 | 4.162 |
| 129 | Machine hall and service bay Layout Plan at 233.5 m | KBL-7230-P-1012 | 4.163 |
| 130 | Control Room Layout Plan at EL 238.0 M Dam toe PH-I | KBL-7230-P-1013 | 4.164 |
| 131 | Control Room Layout Plan at EL 243.0 M Dam toe PH-I | KBL-7230-P-1014 | 4.165 |
| 132 | Power House L-Section through centre line of the unit | KBL-7230-P-1015 | 4.166 |
| 133 | Details of tail race channel dam to PH-I | KBL-7230-P-1016 | 4.167 |
| 134 | Lower level tunnel PH-2 Intake structure-Plan & Sectional Details Sheet 1 of 3 | KBL-7230-P-1101 | 4.168 |
| 135 | Lower level tunnel PH-2 Intake Transition Details Sheet 2 of 3 | KBL-7230-P-1102 | 4.169 |
| 136 | Lower level tunnel PH-2 Trash rack metal Structure Details Sheet 3 of 3 | KBL-7230-P-1103 | 4.170 |
| 137 | Intake service & Emergency gates (4600 x 5500mm) Lower Tunnel Power House –II General installation sheet 1 of 2 | KBL-7230-P-1508 | 4.171 |
| 138 | Intake service & Emergency gates (4601 x 5500mm) Lower Tunnel Power House –II General installation sheet 2 of 2 | KBL-7230-P-1509 | 4.172 |
| 139 | Head race tunnel L- Section Lower level tunnel PH-2 | KBL-7230-P-1104 | 4.173 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 140 | Typical Excavation & Rock Support Details Lower level tunnel PH-2 | KBL-7230-P-1105 | 4.174 |
| 141 | Typical Concrete Lining & Grouting Details Lower level tunnel PH-2 | KBL-7230-P-1106 | 4.175 |
| 142 | Lower level tunnel PH-2 Pressure Shaft /Penstock Steel Liner Details | KBL-7230-P-1108 | 4.176 |
| 143 | Restricted orifice Surge Shaft details Lower level tunnel PH-2 | KBL-7230-P-1107 | 4.177 |
| 144 | 2400mm x 3000 mm Surge shaft gate general installation | KBL-7230-P-1512 | 4.178 |
| 145 | 5000mm x 4000mm Draft Tube Gate for Power House-I I (Daudhan Dam) General Installation | KBL-7230-P-1514 | 4.179 |
| 146 | Lower level tunnel PH-2 (3x6MW) Cross Section | KBL-7230-P-1109 | 4.180 |
| 147 | Lower level tunnel PH-2 MIV Floor layout plan at EL236.5/237.5m | KBL-7230-P-1110 | 4.181 |
| 148 | Lower level tunnel PH-2 (3x6MW) Turbine Floor Layout Plan at EL 242.20 M | KBL-7230-P-1111 | 4.182 |
| 149 | Lower level tunnel PH-2 (3x6MW) Generator Floor Layout Plan at EL 245.70 M | KBL-7230-P-1112 | 4.183 |
| 150 | Service bay and auxiliary bay Floor Layout Plan at EL 250.20 M | KBL-7230-P-1113 | 4.184 |
| 151 | Lower level tunnel PH-2 (3x6MW) L-Section through centre line of the unit | KBL-7230-P-1114 | 4.185 |
| 152 | Lower level tunnel PH-2 details of tail race channel | KBL-7230-P-1115 | 4.186 |

Drawing Volume:IV- Upper Betwa Component-Design

| 153 | Index map of Ken Betwa Link Project |  | 1.1 |
| --- | --- | --- | --- |
| 154 | Calculation for free board of Makodia Dam | KBL-7230-P-251 | 4.187 |
| 155 | Layout Plan of Makodia Dam | KBL-7230-P-258 | 4.188 |
| 156 | Wraparound details Makodia Dam | KBL-7230-P-261 | 4.189 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 157 | Typical- section and details of Makodia Dam | KBL-7230-P-256 | 4.190 |
| 158 | Evaluation of shear Parameters borrow area soils of Makodia Dam | KBL-7230-P-252 | 4.191 |
| 159 | Evaluation of shear Parameters Foundation soils of Makodia Dam | KBL-7230-P-253 | 4.192 |
| 160 | Makodia Earth Dam stability analysis upstream slopes. | KBL-7230-P-254 | 4.193 |
| 161 | Makodia stability analysis downstream slopes. | KBL-7230-P-255 | 4.194 |
| 162 | Cross Section at various RD’s 150.0 m, 490.0 m & 580.0 m Makodia Dam | KBL-7230-P-259 | 4.195 |
| 163 | Surface drainage arrangement Makodia Dam | KBL-7230-P-260 | 4.196 |
| 164 | Foundation treatment Makodia earth dam | KBL-7230-P-257 | 4.197 |
| 165 | General layout plan of Makodia concrete dam | KBL-7230-P-151 | 4.198 |
| 166 | Plan and U/S Elevation of Makodia concrete dam | KBL-7230-P-152 | 4.199 |
| 167 | Maximum non overflow section of Makodia concrete dam | KBL-7230-P-154 | 4.200 |
| 168 | Maximum overflow section of Makodia concrete dam | KBL-7230-P-153 | 4.201 |
| 169 | Zoning of materials (NOF & OF Section) Makodia concrete dam | KBL-7230-P-155 | 4.202 |
| 170 | 13500 x 11500 Spillway Radial Gate Makodia Dam General Installation | KBL-7230-P-1525 | 4.203 |
| 171 | Water stop details O.F. Section Makodia concrete dam | KBL-7230-P-156 | 4.204 |
| 172 | Makodia concrete dam water stop details N.O.F. Section | KBL-7230-P-157 | 4.205 |
| 173 | Pipe outlet at RD- 130 m Makodia Dam | KBL-7230-P-262 | 4.206 |
| 174 | Irrigation outlet at RD 570 m Makodia Dam | KBL-7230-P-263 | 4.207 |
| 175 | Construction sluice details Makodia concrete dam | KBL-7230-P-158 | 4.208 |
| 176 | 3000mm x 4500mm construction Sluice Gates of Makodia Dam General Installation | KBL-7230-P-1529 | 4.209 |
| 177 | Upper Betwa Project Barari Barrage: Detailed Layout Plan | KBL-7230-D-2702 | 4.210 |
| 178 | Upper Betwa Project Barari Barrage: Longitudinal- section of Spillway and Under sluice portion | KBL-7230-D-2703 | 4.211 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 179 | 10000mm x 3720mm Spillway Vertical Lift Fixed Wheel Gate Barari Barrage General Installation | KBL-7230-P-1521 | 4.212 |
| 180 | 10000mm x 7720mm Under Sluice Vertical Lift Fixed Wheel Gate Barari Barrage General Installation | KBL-7230-P-1522 | 4.213 |
| 181 | 10000mm x 1320mm each Spillway Stoplog Gates Barari Barrage General Installation | KBL-7230-P-1523 | 4.214 |
| 182 | 10000mm x 1320mm each under sluice Stoplog Gates Barari Barrage | KBL-7230-P-1524 | 4.215 |
| 183 | Upper Betwa Project Kesari Barrage: Detailed Layout Plan | KBL-7230-D-2709 | 4.216 |
| 184 | Upper Betwa Project Kesari Barrage: LongitudinaL- section of Spillway and Undersluice Portion | KBL-7230-D-2710 | 4.217 |
| 185 | 10000mm x 2400mm Spillway Vertical Lift Fixed Wheel Gates Kesari Barrage General Insallation | KBL-7230-P-1517 | 4.218 |
| 186 | 10000mm x 4900mm Spillway Vertical Lift Fixed Wheel Gates Kesari Barrage Genreal Installation | KBL-7230-P-1518 | 4.219 |
| 187 | 10000mm x 1300mm each Spillway Stoplog Gates Kesari Barrage General Installation | KBL-7230-P-1519 | 4.220 |
| 188 | 10000mm x 1300mm each Under sluice Stoplog Gates Kesari Barrage General Installation | KBL-7230-P-1520 | 4.221 |
| 189 | Upper Betwa Project Makodia Dam:L-Section | KBL-7230-D-2601 to 2656 | 4.222 to 4.277 |
| 190 | Upper Betwa Project Makodia Dam: Details of lined Cross Section of Right Bank Canal | KBL-7230-D-2657 | 4.278 |
| 191 | Upper Betwa Project Makodia Dam: Cross Section of Right Bank Canal | KBL-7230-D-2658 | 4.279 |
| 192 | Upper Betwa Project Makodia Dam: RBC details of Distribution Network | KBL-7230-D-2666 | 4.280 |
| 193 | Upper Betwa Project Makodia Dam: RBC details of Typical Cross Regulator Sheet 1 of 3 | KBL-7230-D-2667 | 4.281 |
| 194 | Upper Betwa Project Makodia Dam: RBC details of Typical Cross Regulator Sheet 2 of 3 | KBL-7230-D-2668 | 4.282 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 195 | Upper Betwa Project Makodia Dam: RBC details of Typical Cross Regulator Sheet 3 of 3 | KBL-7230-D-2669 | 4.283 |
| 196 | Typical Cross Regulator Service Gates of Right Bank Canal-Makodia Dam General installation | KBL-7230-P-1526 | 4.284 |
| 197 | 2000mm x 2000mm Emergency & Service Gates for RBC Intake Makodia Dam General Insallation Sheet No. 1 of 2 | KBL-7230-P-1527 | 4.285 |
| 198 | 2000mm x 2000mm Emergency & Service Gates for RBC Intake Makodia Dam General Insallation Sheet No. 2 of 2 | KBL-7230-P-1528 | 4.286 |
| 199 | Upper Betwa Project Makodia Dam: RBC details of Typical Major Bridge | KBL-7230-D-2660 | 4.287 |
| 200 | Upper Betwa Project Makodia Dam: RBC details of Typical Syphon Aqueduct | KBL-7230-D-2663 | 4.288 |
| 201 | Upper Betwa Project Makodia Dam: Super Passage | KBL-7230-D-2665 | 4.289 |
| 202 | Upper Betwa Project Makodia Dam LBC: L-Section RD 0.0 Km to 1.50Km | KBL-7230-D-2671 | 4.290 |
| 203 | Upper Betwa Project Makodia Dam LBC: L- section RD 1.5 Km to 3.0Km | KBL-7230-D-2672 | 4.291 |
| 204 | Upper Betwa Project Makodia Dam LBC: L- section RD 3.0 Km to 4.5 Km | KBL-7230-D-2673 | 4.292 |
| 205 | Upper Betwa Project Makodia Dam LBC: L- section RD 4.5Km to 6.0Km | KBL-7230-D-2674 | 4.293 |
| 206 | Upper Betwa Project Makodia Dam LBC: L- section RD 6.0Km to 6.7 Km | KBL-7230-D-2675 | 4.294 |
| 207 | Upper Betwa Project Makodia Dam LBC: Cross Section | KBL-7230-D-2676 | 4.295 |
| 208 | Upper Betwa Project Barari Barrage:L- section of Canal RD 0.0Km to 1.55Km | KBL-7230-D-2705 | 4.296 |
| 209 | Upper Betwa Project Barari Barrage:L- section of Canal RD 1.55Km to 3.0Km | KBL-7230-D-2706 | 4.297 |
| 210 | Upper Betwa Project Barari Barrage:L- section of Canal RD 3.0Km to 4.5Km | KBL-7230-D-2707 | 4.298 |
| 211 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 2.9Km to 4.45Km | KBL-7230-D-2720 | 4.299 |
| 212 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 4.45Km to 5.95Km | KBL-7230-D-2721 | 4.300 |
| Sl. No. | Title | CWC drawing No. | Plate No. |
| 213 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 5.95Km to 7.4Km | KBL-7230-D-2722 | 4.301 |
| 214 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 7.4Km to 8.9Km | KBL-7230-D-2723 | 4.302 |
| 215 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 8.9Km to 10.4km | KBL-7230-D-2724 | 4.303 |
| 216 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 10.4Km to 11.95Km | KBL-7230-D-2725 | 4.304 |
| 217 | Upper Betwa Project Kesari Barrage: L- section of Canal RD 11.95Km to 12.50Km | KBL-7230-D-2726 | 4.305 |
| Ken – Betwa H.E. Project, 2 x 30 MW | CEA drawing No. |  |
| 218 | General Layout plan. | 1252-CEA-HE&RM- KB- DPR-01 | 5.1 |
| 219 | Power House Cross Section | 1252-CEA-HE&RM- KB –DPR-02 | 5.2 |
| 220 | Power House Generator floor layout at EL 229.00 m | 1252-CEA-HE&RM- KB –DPR-03 | 5.3 |
| 221 | Power House Turbine floor layout at EL 225.00 m | 1252-CEA-HE&RM- KB –DPR-04 | 5.4 |
| 222 | Power House MIV floor layout at EL 218.00 m | 1252-CEA-HE&RM- KB –DPR-05 | 5.5 |
| 223 | Power House Machine Hall & Service bay layout at EL 233.00m | 1252-CEA-HE&RM- KB –DPR-06 | 5.6 |
| 224 | Power House Control Room layout at EL 238.00 m | 1252-CEA-HE&RM- KB –DPR-07 | 5.7 |
| 225 | Power House – Auxiliary Bay and Transformer deck layout at EL 243.00 m | 1252-CEA-HE&RM- KB –DPR-08 | 5.8 |
| 226 | Power House L-Section through Center line of the Units | 1252-CEA-HE&RM- KB –DPR-09 | 5.9 |
| 227 | Single Line Diagram (for PH-I and PH-II) | 1252-CEA-HE&RM- KB –DPR-10 | 5.10 |
| 228 | Layout Plan of 132 kV Switchyard & Sections | 1252-CEA-HE&RM- KB –DPR-11 | 5.11 |
|  | Ken – Betwa H.E. Project, 3 x 6 MW |  |  |
| 229 | Layout Plan of 33 kV Switchyard & Sections for power house-II | 1252-CEA-HE&RM- KB –DPR-08 | 5.12 |
| Sl. No. | Title | CEA drawing No. | Plate No. |
| 230 | General Layout plan. | 1252-CEA-HE&RM- KB- DPR-01 | 5.13 |
| 231 | Power House Cross Section | 1252-CEA-HE&RM- KB -DPR-02 | 5.14 |
| 232 | Power House Auxiliary Bay, Service Bay and Transformer deck layout at EL 250.20 m | 1252-CEA-HE&RM- KB -DPR-03 | 5.15 |
| 233 | Power House Generator floor layout at EL 245.70 m | 1252-CEA-HE&RM- KB -DPR-04 | 5.16 |
| 234 | Power House Turbine floor layout at EL 242.20 m | 1252-CEA-HE&RM- KB -DPR-05 | 5.17 |
| 235 | Power House MIV floor layout at EL 236.50/237.50m | 1252-CEA-HE&RM- KB -DPR-06 | 5.18 |
| 236 | Power House L-Section through Center line of the Units | 1252-CEA-HE&RM- KB -DPR-07 | 5.19 |
| 237 | Single Line Diagram (for PH-I and PH-II) | 1252-CEA-HE&RM- KB -DPR-09 | 5.20 |